## Slide 1: COMS31700 Design Verification Hardware Design Languages
Kerstin Eder
(Acknowledgement: Avi Ziv from the IBM Research Labs in Haifa has kindly permitted the re-use of some of his slides.)
Department of
COMPUTER SCIENCE

## Slide 2: Hardware Design Languages
Hardware Design Languages were built with simulation in mind
  Synthesis and other back-end purposes were added at a later stage
Most popular languages today (both are IEEE standards)
  VHDL
  Verilog/SystemVerilog
VHDL:
  Committee-designed language contracted by U.S. (DoD) (ADA-derived)
  Functional/logic modeling and simulation language
  Main differentiator from Verilog is types (e.g. records)
Verilog:
  Logic modeling and simulation language
  Started in EDA industry in the 80's then owned by Cadence
  Donated to IEEE as a general industry standard
  SystemVerilog (the next generation of Verilog) is designed to improve abstraction of Verilog
    Abstraction levels
    Data types
    Verification constructs
Verilog vs. VHDL: personal preferences, EDA tool availability, commercial, business and marketing issues.

## Slide 3: Modeling Levels – Major Dimensions
Temporal Dimension:
  continuous (analog)
  gate delay
  clock cycle
  instruction cycle
  events
Data Abstraction:
  continuous (analog)
  bit : multiple values
  bit : binary
  abstract value
  composite value ("struct")
Functional Dimension:
  continuous functions (e.g. differential equations)
  Switch-level (transistors as switches)
  Boolean Logic
  Algorithmic (e.g. sort procedure)
  Abstract mathematical formula (e.g. matrix multiplication)
Structural Dimension:
  Single black box
  Functional blocks
  Detailed hierarchy with primitive library elements
discrete time
discrete value

## Slide 4: Modeling Levels – Major Dimensions
Continuous
Gate Delay
Clock Cycle
Instruction Cycle
Events
Continuous
Multivalue Bit
Bit
abstract value
"struct"
Continuous
Switch Level
Boolean Logic
Algorithmic
Abstract Mathematical
Single Black Box
Functional Blocks
Detailed Component Hierarchy
Temporal
Data
Functional
Structural
Verilog SystemVerilog
VHDL Extremely inefficient

## Slide 5: Verilog for Design Verification
Assignment calc1 design in Verilog
  Testbench for calc1 design in Verilog
Interactive Evita Verilog tutorial (Ch1-4,5-7):
  Structure of Verilog modules
  Verilog signal values: 0, 1, x and z (4-valued logic)
  Verilog signals:
    nets (used for “connections”, no storage capacity)
    registers (storage capacity, similar to variables in pgr languages)
  Verilog external signals:
    ports (input, output or inout, port connecting rules)
  Coding styles:
    Structural
    Dataflow
    Behavioural (best for verification)

## Slide 6: Continuous Assignment
Used in Dataflow coding style.
Keyword assign followed by optional delay declaration
LHS (target) can be net (scalar or vector) or concatenation of nets
  NO registers allowed as target for assignment!
Assignment symbol: =
RHS is an expression.
  assign #4 Out = In1 & In2;
Implicit continuous assignment: wire x = ...;
Conditional assignment:
  assign Out = Sel ? In1 : In0;
  If Sel is 1 then In1 is assigned to Out; if Sel is 0 then Out is In0.
  If Sel is x/z, evaluate both In1 and In0, if they are the same then Out is assigned this value, otherwise x/z.

## Slide 7: Continuous Assignment: Execution
Continuous assignments are always active.
Concurrency:
  When any of the operands on RHS changes, assignment is evaluated.
  Several assignments can be executed concurrently.
  Race conditions can occur!
    Two or more assignments, which operate on the same data, read and write the data concurrently.
    Result, which might be erroneous, depends on which assignment does what when.
Delays specify time between change of operand on RHS and assignment of resulting value to LHS target.
  assign #4 Out = In1 & In2;

## Slide 8: Behavioural Coding Style
Most advanced coding style: flexible and high-level
  closest to programming languages
  allows use of conditional statements, case statements, loops, etc.
Best for verification, but by no means ideal...
Behaviour:
  Actions a circuit is supposed to perform when it is active.
Algorithmic description: Need ”variables” similar to PLs!
  Abstraction of data storage elements - register objects:
    reg R; one bit register - default value x before first assignment
    time T; can store/manipulate simulation time
    integer N; by default at least 32 bit - stores values signed
    real R; default value is 0
    [Other data types, e.g. arrays exist, but are out of the scope of this introduction.]

## Slide 9: Behavioural Constructs for Coding
Conditionals:
if (expression true) true branch; else false branch;
Case:
case ({_,...,_})
pattern : ...;
...
default : ...;
endcase
Loops: forever, repeat, while, for
See Verilog reference card for syntax!

## Slide 10: Mux421: Behavioural Coding Example
module mux421_behavioural (Out, In0, In1, In2, In3, Sel0, Sel1);
output Out;
input In0, In1, In2, In3, Sel0, Sel1;
reg Out;
always @ (Sel1 or Sel0 or In0 or In1 or In2 or In3)
begin
case ({Sel1,Sel0})
2’b00 : Out = In0;
2’b01 : Out = In1;
2’b10 : Out = In2;
2’b11 : Out = In3;
default : Out = 1’bx;
endcase
end
endmodule // mux421_behavioural

## Slide 11: Mux421: Behavioural Coding Example
module mux421_behavioural (Out, In0, In1, In2, In3, Sel0, Sel1);
output Out;
input In0, In1, In2, In3, Sel0, Sel1;
reg Out;
always @ (Sel1,Sel0,In0,In1,In2,In3) // Verilog 2001 style
begin
case ({Sel1,Sel0})
2’b00 : Out = In0;
2’b01 : Out = In1;
2’b10 : Out = In2;
2’b11 : Out = In3;
default : Out = 1’bx;
endcase
end
endmodule // mux421_behavioural

## Slide 12: Behavioural Blocks
initial and always
  Can’t be nested.
  Block containing several statements must be grouped using:
    begin ... end (sequential) or
    fork ... join (concurrent)
initial block:
  Used to initialise variables (registers).
  Executed at (simulation) time 0. Only once!
always block:
  Starts executing at time 0.
  Contents is executed in infinite loop.
    Means: Executing repeats as long as simulation is running.
  Multiple blocks are all executed concurrently from time 0.

## Slide 13: Assignment in Behavioural Coding
Assignment in behavioural coding style is procedural:
LHS (target) must be a register (reg, integer, real or time) - not a net, a bit or part of a vector of registers.
NO assign keyword!
Must be contained within a behavioural (i.e. initial or always) block.
NOT always active!
  Target register value is only changed when procedural assignment is executed according to sequence contained in block.
Delays: indicate time that simulator waits from ”finding” the assignment to executing it.

## Slide 14: Blocking Assignment
(... as opposed to continuous assignment from dataflow coding style.)
  reg A;
  reg [7:0] Vector;
  integer Count;
  initial
  begin
  A = 1’b0;
  Vector = 8’b0;
  Count = 0;
  end
Sequential initialisation assignment.

## Slide 15: Timing Control Evaluation
    1. Find procedural assignment
    2. Wait 5 time units
    3. Perform A+B
    4. Wait 10 time units
    5. Assign result to C
So, what is the difference between:
  #10 C = A+B and
  C = #10 A+B?
#5 C = #10 A+B;
Assignment delay
Intra-assignment delay

## Slide 16: Events and Wait
Events mark changes in nets and registers, e.g. raising/falling edge of clock.
  @ negedge means from any value to 0
  @ posedge means from any value to 1
  @ clk always activates when clock changes
Wait statement:
  wait (condition) stmt;
    wait (EN) #5 C = A + B;
      waits for EN to be 1 before #5 C = A + B;
Use wait to block execution by not specifying a statement!
  wait (EN); ...

## Slide 17: Sensitivity List
Allows to suspend always blocks.
Block executes and suspends until signal (one or more) in sensitivity list changes.
NOTE: or is used to make statement sensitive to multiple signals or events.
(Don’t use sensitivity list to express a logical condition!)
Common mistake:
  Forgetting to add relevant signals to sensitivity list!
always @(sensitivity list) <begin> <procedural stments> <end>
always @ (posedge Clk or EN)
begin ... end
always @ (Sel1,Sel2) // Verilog 2001 style
begin ... end

## Slide 18: Non-blocking Assignments
Concurrency can be introduced into sequential statements.
  Delay is counted down before assignment,
  BUT control is passed to next statement immediately.
Non-blocking Assignments allow to model multiple concurrent data transfers after common event.
A blocking assignment would force sequential execution.
A <= #1 1; B <= #2 0; (non-blocking)
    A x 1 1 1
    B x x 0 0
    Time: 0 1 2 3
A = #1 1; B = #2 0; (blocking)
    A x 1 1 1
    B x x x 0
    Time: 0 1 2 3

## Slide 19: Approaches to Assignment - I
reg [7:0] MyReg;
initial
fork
#50 MyReg = 8’hFF;
#100 MyReg = 8’h01;
#150 MyReg = 8’h2F;
#200 MyReg = 8’h00;
#250 $finish;
join
Concurrent blocking (=)
    Time: 0 50 100 150 200 250
MyReg[7:0] XX FF 01 2F 00 00
Important when driving input into a DUV in a testbench!

## Slide 20: Approaches to Assignment - II
reg [7:0] MyReg;
initial
begin
MyReg <= #50 8’hFF; // pass control, wait, assign
MyReg <= #50 8’h01;
MyReg <= #50 8’h2F;
MyReg <= #50 8’h00;
#250 $finish;
end
Sequential non-blocking (<=)
    Time: 0 50 100 150 200 250
MyReg[7:0] XX
Important when driving input into a DUV in a testbench!
Race Condition!
??

## Slide 21: Approaches to Assignment - III
reg [7:0] MyReg;
initial
begin
MyReg <= #50 8’hFF; // pass control, wait, assign
MyReg <= #100 8’h01;
MyReg <= #150 8’h2F;
MyReg <= #200 8’h00;
#250 $finish;
end
Sequential non-blocking (<=)
      Time: 0 50 100 150 200 250
      MyReg[7:0] XX FF 01 2F 00 00
Important when driving input into a DUV in a testbench!

## Slide 22: Approaches to Assignment - IV
reg [7:0] MyReg;
initial
begin
#50 MyReg = 8’hFF; // wait, assign, pass control
#50 MyReg = 8’h01;
#50 MyReg = 8’h2F;
#50 MyReg = 8’h00;
#250 $finish;
end
Sequential blocking (=)
      Time: 0 50 100 150 200 250
      MyReg[7:0] XX FF 01 2F 00 00
Important when driving input into a DUV in a testbench!

## Slide 23: HDL vs. Programming Languages
3 major new concepts of HDLs compared to PLs:
Connectivity:
  Ability to describe a design using simpler blocks and then connecting them together.
Time:
  Can specify a delay (in time units of simulator): (WHY?)
    and #2 (Y3, In3, Sel1, Sel0);
Concurrency is always assumed! (for structural style this is)
  No matter in which order primitives/components are specified, a change in value of any input signal activates the component.
  If 2 or more components are activated concurrently, they perform their actions concurrently.
  Order of specification does not influence order of activation!
  (NOTE: Statements inside behavioural blocks may be sequential -more later.)

## Slide 24: Tasks and Functions

## Slide 25: Tasks and Functions
Both are purely behavioural.
  Can’t define nets inside them.
  Can use logical variables, registers, integers and reals.
Must be declared within a module.
  Are local to this module.
  To share tasks/functions in several modules, specify declaration in separate module and use ‘include directive.
Timing (simulation time)
  Tasks:
    No restriction on use of timing; engineer specifies execution.
  Functions:
    Execute in ZERO sim time units; no timing/event control allowed.

## Slide 26: Comparing Tasks with Functions
 | Tasks | Functions
Timing | can be non-zero sim time | execute in 0 sim time
Calling other tasks or functions | no limit; may enable functions | may not call tasks but may call another function No recursion!
Arguments | any number; any type; can’t return result | at least one input; no output/inout; always results in single return value
Purpose | modularize code | react to some input with single response; only combinatorial code; use as operands in expressions

## Slide 27: Example Task
task factorial;
output [31:0] f;
input [3:0] n;
integer count; // local variable
begin
f = 1;
for (count=n; count>0; count=count-1)
f = f * count;
end
endtask
Invoke task: < task name > (list of arguments);
  Declaration order determines order of arguments when task is called!

## Slide 28: Example Function
function ParityCheck;
input [3:0] Data;
begin
ParityCheck = ˆData; // bit-wise xor reduction
end
endfunction
Result is by default a 1 bit register assigned to implicitly declared local variable that has same name as function.
Function calls:
  Are either assigned to a variable, or
  occur in an expression that is assigned to a variable,
  or occur as an argument of another function call.

## Slide 29: System Tasks and Functions
More than 100 Verilog system tasks/functions.
  (See Evita Verilog Reference Guide for more information.)
Can be used in any module without explicit include directive.
Syntax: $< keyword >
Most important tasks for verification:
  $display, $monitor
  $time, $stop, $finish
  (Also with files: $fopen, $fdisplay)

## Slide 30: Summary
Evita Verilog Tutorial [Ch1-7]
Verilog HDL IEEE Standard 1364-2001
  Signals: internal and external (ports)
  Different coding styles:
    structural
    dataflow
    behavioural
SystemVerilog builds on IEEE 1364-2005
HDLs: Connectivity, Time and Concurrency
BOOK: Verilog HDL by Samir Palnikar [in QB Library]
Next: Specification of Assignment 1!