## Slide 1: COMS31700 Design Verification: Are we there yet? (The back-end of the verification cycle)
Kerstin Eder
(Acknowledgement: Avi Ziv from the IBM Research Labs in Haifa has kindly permitted the re-use of some of his slides.)
Department of
COMPUTER SCIENCE

## Slide 2: Outline
The verification cycle - revision
Coverage Closure
Analysis and adaptation
  (Coverage analysis)
  Failure analysis
Regression
Tape-out readiness
Escape analysis

## Slide 3: The Verification Cycle
Functional
Specification
Designer implements
the functional specification
(in HDL)
Create
Verification
Plan
Develop Verification Environment
Stimulus, checkers,
Formal Verification
Debug HDL and
Environment
Run Regression
Perform Escape
Analysis
Debug Fabricated
Hardware
Lessons
Learned
Tape Out
Readiness
Plan
Review

## Slide 4: My Environment Is Ready. Now What?
More functionality is added to the design
  And therefore, to the verification environment
Mature enough design is progressed to the next level in the design hierarchy
  Unit to core to chip to system
Bugs are being discovered and fixed
  And bug fixes need to be verified
The implementation of the verification plan continues
  Closing holes in coverage
  Updating the verification plan itself as needed
Regression is being executed to ensure everything still works

## Slide 5: Coverage Closure

## Slide 6: Coverage Closure
Coverage closure is the process of:
Finding areas of coverage not exercised by a set of tests.
  Coverage Holes!
Creating additional tests to increase coverage by targeting these holes.
  Beware: Aim to “balance” coverage!

## Slide 7: Controllability Problems
If the cases to be hit contain internal states/signals of the DUV, directed tests that exercise all combinations are hard to find.
    Processor pipeline verification: Control logic, Internal FSMs
Generate biased random tests automatically. [RTPG]
    ISG
  Typically tests are filtered to retain only those that add to coverage.
  Coverage analysis indicates hard-to-reach cases.
  Don’t waste engineers time on what automation can achieve.
Combine automatically generated stimulus with coverage.
Gives rise to Coverage DRIVEN Verification Methodology
BUT:
Hard-to-reach cases (may) need manual attention.
  Bias tests towards certain conditions or corner cases.
  Supplying bias requires significant engineering skill.
    Often only trial-and-error approach.

## Slide 8: Biasable Random Test Generation
[A Adir, E Almog, L Fournier, E Marcus, M Rimon, M Vinov and A Ziv. Genesys-Pro: Innovations in Test Program Generation for Functional Processor Verification. In IEEE Design & Test of Computers, 2004.]
Test template description language
  expressiveness of programming language
  virtually unlimited control over events to be generated
Architectural modelling framework
  building blocks at high enough level to describe processors
    VLIW architectures
Generation engine based on constraint satisfaction
  generic constraint solver customized for pseudo-random test generation

## Slide 9: Coverage DRIVEN Verification Methodology
Run tests
Collect coverage
Create initial coverage model
Generate tests
Add tests to target holes
Review / enhance coverage models if needed
Identify coverage holes
From Verification Plan:
Current research: How can we automate this further?

## Slide 10: 80/20 Split
In practice: 80/20 (20/80) split wrt coverage progress.
Good news:)
80% of coverage is achieved (relatively quickly/easily) driving randomly generated tests.
This takes about 20% of total time/effort/sim runs spent on verification.
Bad news:(
Gaining the remaining 20% coverage,
  i.e. filling the remaining coverage holes (which often needs to be done manually and requires a lot of skill plus design understanding),
can take as much as 80% of the total time/effort/sim runs spent on verification.

## Slide 11: Benefits of Coverage DRIVEN Verification Methodology
Benefits:
  Shortens implementation time
    (Initial setup time)
    Random generation covers many “easy” cases
  Improves quality
    Focus on goals in verification plan
    Encourages exploration/refinement of coverage models
  Accelerates verification closure
    Refine/tighten constraints to target coverage holes

## Slide 12
Run tests
Collect coverage
Create initial coverage model
Generate tests
Add tests to target holes
Review / enhance coverage models if needed
Identify coverage holes
From Verification Plan:
Current research: How can we automate this further?
Coverage DRIVEN Verification Methodology

## Slide 13: Coverage DIRECTED Test Generation
Run tests
Collect coverage
Create initial coverage model
Generate tests
Add tests to target holes
Review / enhance coverage models if needed
Identify coverage holes
From Verification Plan:
Current research: How can we automate this further?
Machine Learning

## Slide 14: CDG: Coverage DIRECTED Test Generation
How can we make better use of coverage data to automate stimulus generation?
Latest Research:
Coverage DIRECTED (stimulus/test) generation [IBM]
BY CONSTRUCTION
  Require description of design as FSM.
  Use formal methods to derive transition coverage.
  Automatically translate paths through FSM to test vectors.
  Fall over in practice: FSMs are prohibitively large!
BY FEEDBACK
  (Exploit Machine Learning techniques)
  GAs/GP - Need to find suitable encoding (e.g. of instructions).
  Bayesian Networks - Need to design and train BN.
  Data Mining in coverage spaces
No significant breakthrough in CDG yet!

## Slide 15: Summary: Coverage Closure
Verification Methodology should be coverage driven.
Automation: Research into coverage directed test generation
Delays in coverage closure are the main reason why verification projects fall behind schedule!

## Slide 16: Analysis and Adaptation Regression

## Slide 17: Analysis and Adaptation
Building a good verification plan is the first step for successful verification
  But, it is not enough!
Need to constantly:
  Monitor the verification process
  Analyze the observations
  Adapt to address issues identified by the analysis
Three basic levels of adaptation
  Change the way the verification environment is activated
  Change the verification environment
  Change the verification plan
Notes: So far, we discussed how to build a good verification plan. This is a necessary first step for successful verification, but a good plan alone is not sufficient for a successful verification. The reason for that is no matter how careful and detailed our plan is, we cannot foresee everything that will happen during the execution of the plan. Specifically, we cannot foresee when and where bugs will be found. In addition, even a perfect plan cannot guarantee success if its execution is not good enough.
Therefore, throughout the execution of the VP, we need to constantly monitor the verification process, analyze the observations we get, and adapt to address the issues that are pointed out by the observations and the analysis.
Adaptation can lead to changes in all aspects of the verification process, starting from its foundations, namely the verification plan. Simply speaking, the adaptation can be at three basic levels. The simplest level is changes in the way the verification environment is activated. Changes at this level can include adding new stimuli specifications for the stimulus generator or simply changes the number of simulation jobs executed for existing specifications. More complex adaptation require changes to verification environment itself, and in some cases the verification plan need to be adapted to address some issues. Note that changes at a basic level may often require changes at the levels above it as well.

## Slide 18: Two Types of Analysis
Coverage analysis
  Was included in the lectures on coverage.
Failure analysis
Notes: The observation data and analysis can come from many sources, and many observations analysis and adaptation come from project management in general, engineering projects specifically, and even more specifically, SW development. Here, we concentrate on items that are specific to verification, namely coverage analysis and failure analysis. Coverage analysis is the main vehicle for measuring the progress of verification against the plan; while failure analysis can help us identify problems in the plan itself.

## Slide 19: Failure Analysis
Skip to Regression

## Slide 20: Failure Analysis
During execution of the verification plan (many) failures are observed
This is not a bad phenomena
  Remember that the goal of the verification process is to identify faults in the DUV
The goal of failure analysis is to understand failures, their causes, their relation to one another, and their relation to the verification process
Notes: During the execution of the verification plan failures occur. It is important to note that this phenomenon is not necessarily bad, because, after all, the goal of the verification process is to demonstrate that the implementation adheres to the requirements and the specification and this is usually done by removing faults or bugs that prevent it from doing so. The goal of failure analysis is to learn as much as possible from failures and their causes. Failure analysis should lead to fixing everything that needs to be fixed, and this is more than just removing the bug from the implementation. In fact, here we focus on analysis that helps fixing the verification plan and its execution.

## Slide 21: Failures and Faults
Failure – an observed DUV behavior that violates the specified behavior
Fault – the root cause of a failure
There can be a many-to-many relationship between faults and failures
  Mishandling of overflow in the input FIFO can cause:
    Lost commands in the output port
    Bad data in the output port
  Bad data in the output port can be caused by:
    Mishandling of overflow in the input FIFO
    Bad selection in the output selector
Notes: Before talking about analysis, some terminology and the difference between failure and fault. Failure is an observation that the behavior of the implementation is not what it should be. Fault is the root cause of the failure. Permanent logical and functional faults are often called bugs, and in the discussion here we may interchange faults and bugs. For example, if by mistake we replace an and gate with an or gate in an adder, a possible failure is getting 1 + 1 = 3, while the fault is the gate replacement.
It is important to note that in many cases there is many-to-many relation between faults and failures. For example, a fault of mishandling overflow in the input queue of the DMA engine can lead to lost commands in the output port or bad data there (two different failures) and bad data may be caused by this mishandling of overflow or selecting a wrong data source.

## Slide 22: How Failures Are Detected
Inspection and code review
Output of formal verification tools or other static analysis tools, such as lint
Activation of response checkers during simulation
Analysis of coverage data
Visual observation of application misbehavior
Notes: Failures can be detected in many ways ranging from inspection and reviews (not only of code, but also requirements, specification, verification plans, and more) to visual observation of real-life application misbehavior.

## Slide 23: Types of Failure Analysis
Detailed failure analysis
  Understand the cause and effects of failures and faults on the design, environment, verification process and more
Statistical failure analysis
  Identify trends, provide prediction
Notes: We can divide failure analysis into two main categories. Detailed analysis looks at a failure or fault (or a small group of them) and tries to understand the cause and effects of the failure. Statistical analysis looks at larger sets of failures and tries to extract statistical information out of them, such as trends and predictions. Statistical analysis is similar in many ways to coverage progress analysis.

## Slide 24: Detailed Failure Analysis
The outcome of the analysis
  The failure is understood and recorded
  The failure is resolved
  The verification plan and process are adapted
  Lessons learned for the future
Note: In most cases failure analysis—and especially the last two items—are simple and the outcome of the analysis is that we found a failure and a fault when and where expected and because we are doing our job the right way.
Notes: We start with detailed analysis, and for the detailed analysis we start at the end. Namely, what is the outcome of the analysis? The outcome has several elements in it. First, we need to ensure that the failure is understood and recorded (this can save a lot of time and effort when similar failures are found in the future). Next, the failure needs to be resolved. This does not necessarily mean that the fault leading to it is fixed. The last two elements concern the verification process. First, we need to ensure that the verification plan and process are adapted accordingly, and that any important lessons learned are applied in the future.
While this sounds scary, it is important to note that in most cases the last two elements are very simple. They say that we found a failure because we were looking for it and we did our job properly.

## Slide 25: Understanding the Failure
The goal is to understand the scope and severity of the failure and how the failure can be recreated
Provides useful information for debugging and other parts of the failure analysis
  Simplify and generalize the failure conditions
    Find simper settings / stimuli that recreate the failure
    Find necessary and sufficient conditions for the failure
  Localize the fault in terms of place and time
  Research: Generate easy-to-debug tests
Notes: The first thing is to understand the failure in term of its effects. An important aspect here is to find how to recreate the failure because this will lead to the underlying fault. When doing so, we would like to extract as much useful information for debugging and other parts of the analysis. Important aspects here is simplifying and generalizing the failure conditions and localizing it as much as possible.

## Slide 26: What to Look For
In simulation
  Determinism
    Does the failure always occur in the same settings?
      With the same seed?
      With different seeds (or random seed)?
  Parameters that are correlated with the failure
    Parameters that cause the failure to disappear
    Parameters that cause the failure to change
  Specific parts in the stimuli that are correlated to the failure
In formal verification
  Constraints that affect the failure
  Time bounds that affect the failure
Notes: Important aspect in understanding a failure is understanding the conditions in under it occurs. In simulation, the first thing to check is how deterministic is the failure. In other words, does it always occur in the same settings (with and without the same random seed). Next, it can be useful to understand which parameters in the environment are correlated to the failure. Specifically, we look for parameters that cause the bug to disappear or change behavior. More useful—but in many cases harder to obtain information—is direct correlation between the applied stimulus and the failure. The equivalent to this in formal verification is the constraints and bounds applied in the formal verification process.

## Slide 27: Resolving the Failure
This does not always mean fix the fault
  Defer to future tape outs / releases
  Bypass by software or surrounding modules
  Record in errata sheets
Need to ensure that the resolution is complete
  The fix / bypass is correct
  All cases are covered
  No new faults introduced in the process
  (Similar cases are also handled)
Mini-verification plan is needed
  Coverage models
  Stimuli generation strategy
  New result checkers
Notes: The next step is resolving the failure. As mentioned earlier, this does not always mean fixing the bug. No matter what resolution is used, it is important that it is correct and complete and that it did not introduce new failures. It is also important to check that similar faults—sometimes called “cousin bugs” —do not exist or are fixed as well. This call for a mini-verification plan for the fix (but again this mini-plan can be quite small).

## Slide 28: Adapting the Verification Plan and Process
Need to minimize faults found by chance or found too late
  These faults can easily be missed if we are less lucky
Indicators that faults are found by chance
  Faults are not found at the right time
    Fault is found at the wrong level of the hierarchy
    Faults are found not at the area we concentrate on
    Need to understand why faults are not found at the right time
      And, change the plan and process accordingly
  Faults are not found by the right checker
    Only a side effect of the fault is detected
    May indicate missing checker or problems in existing checker
  Simulation with failure is not flagged by coverage
    Does not activate uncovered or rarely covered coverage point
    Indicates missing coverage models
Notes: The goal of adaptation is to reduce the number of faults found by chance. Finding faults accidentally is dangerous because these faults can easily be missed if we are less lucky. Therefore, an important part of failure analysis is looking for indications that a fault was found by chance, fixing the verification plan and its implementation to ensure that similar faults are found because we are looking for them. Indications that a fault is found by chance are:
  Wrong place or time — wrong level of the hierarchy (e.g., the adder bug is found only at system verification); failures at areas that we do not concentrate on (e.g., the adder bug is found while concentrating on the multiplier). We need to understand why the fault was not caught at the right time and fix the plan accordingly. For example, adding coverage model for the adder operation would have prevented this problem.
  Fault is found by the wrong checker — For example the adder bug is found because it caused wrong data length in outgoing message. Here, we need to ensure that proper checkers that catch such failures close to their occurrence are added.
  Simulation is not flagged by coverage — If the simulation with failure does not hit an uncovered or rarely covered event, then that simulation is not different from other simulation from coverage point of view. This means that a coverage point or coverage model that corresponds to the failure is missing.

## Slide 29: Correlating Coverage and Failures
There is a direct correlation between
  Changes in the verification environment and the DUV
  Progress in coverage
  Detection of new failures
Coverage
Environment
Failures
Notes: An important aspect of analysis and adaptation is the correlation between coverage and failures, correlation between the two of them and changes in the design and environment. For example, activating a new feature in the design should open the door for new bugs to show themselves (as we saw earlier) and also improve coverage.

## Slide 30: Correlating Failure Rate and Coverage Progress
Notes: This plot shows the failure rate (the blue plot, note error in printed version) and coverage progress as a function of time. The plot shows that most failures are exposed when coverage increases at the fastest pace. The explanation for this is simple. When coverage progresses faster, it means that more areas of the design are explored at the same time, and therefore, the potential of finding new problems increases.

## Slide 31: Individual Coverage and Failure Correlation
Correlating a failure to specific coverage can be helpful in the failure analysis and debugging processes
Rare coverage points exercised by a simulation that fails can hint at the location of the fault that caused the failure
  Rare coverage points are coverage points rarely, if ever, exercised by passing simulations
  These coverage points record what happened in the DUV prior to the failure
  They are very useful if the failure is distant (in logic or time) from the fault or the fault is complex
If no such rare coverage points are recorded, then it is likely that the failure is found by chance
  The verification plan needs to be refined to catch these failures
Notes: Correlating a specific failure with a coverage point can be useful in the failure analysis process. If a failed simulation hits rare coverage points, these points can provide hints about the location of the fault that caused the failure. The rare events are a trail of what happened in the DUV prior to the failure, thus they can indicate where the fault might be. This is especially true if the failure is far from the fault or the fault is complex.
On the other hand, if the failed simulation does not contain rare coverage points, it is likely that the failure was found by chance. In this case we should investigate what is missing in the verification plan and how to refine it so that such failures would not escape.

## Slide 32: Regression

## Slide 33: Regression Suites
A regression suite is a set of tests that are run on the verified design on a regular basis
  After major changes
  Periodically: Every night or every weekend
Regression goals
  Assuring that things that worked did not stop working
    This is vital because every bug fix, on average, introduces one fifth of a bug
  Detecting “unexpected” bugs

## Slide 34: Types of Regression
Static regression
  The regression suite is comprised of a set of “interesting” test patterns
    Tests that found bugs in the past
    Tests that reach corner cases
Random regression
  A.k.a. dynamic regression, probabilistic regression
  The regression suite is comprised of a set of test specifications and an execution policy
    For example, execute 100 tests of specification A, 35 tests of specification B, and 20 tests of specification C

## Slide 35: Static Vs. Random Regression
Static regression
  Known, guaranteed quality
  Sensitive to changes
  Hard to maintain
Random regression
  Unknown quality
  Less sensitive to changes
  Easy to maintain
  Easy to adapt to simulation resources

## Slide 36: The Preferred Solution
Combination of static and random suites
Small static suite with hard to recreate cases
  Hard to reach corner cases
  Tests that discovered hard to find bugs
Random suites for everything else

## Slide 37: Regression Suites Requirements
A regression suite must be:
  Comprehensive so that it is likely to catch all the bugs introduced
  Small so that it can economically be executed many times
How can we make our regression suite small and comprehensive?
Solution: use coverage information
  Select a set of tests that achieve 100% coverage (of the coverage achieved so far)
  Select the smallest possible such set

## Slide 38: The Set Cover Problem
Let S = {C1,...,Cn} be the set of coverage tasks
Let T = {T1,...,Tn} be a set of tests
  Each test Ti covers subset {Ci1, Ci2, ...} of the coverage tasks
The set cover problem: Find the smallest subset of T that covers S
The set cover problem is a known NP-Complete problem
  However, there are a number of good algorithms for it

## Slide 39: Online Algorithm
For each new test T
  If T covers an uncovered coverage task
    Add T to the regression suite
Advantages
  Very simple
  Low memory requirements

## Slide 40: Online Algorithm Example
4
8
Test Coverage
Accumulated Coverage
Regression Suite
Uncovered
Covered
Newly covered
3
3
5
5
6
6
7
7
9
9
1
1
2
2

## Slide 41: Greedy Algorithm
Initialization
  Build coverage matrix tests vs. tasks
  Select tests that uniquely cover tasks
Loop until all covered tasks are removed
  Remove all the tasks covered by selected tests
  Choose the test that covers most remaining tasks
Advantages
  Complexity is polynomial in the number of tests and coverage tasks
  Quality solution
Disadvantage
  Requires to keep the entire coverage matrix in memory

## Slide 42: Greedy Algorithm Example
4
8
Test Coverage
3
5
6
7
9
1
2
1
2
3
4
5
6
7
8
9
2
2
4
4
2
8
1
6
4
a b c d e f g h i j k l m n o p
1. Build Coverage Matrix
Covered tasks
2. Select tests that uniquely cover tasks
Regression Suite: 5, 9

## Slide 43: Greedy Algorithm Example
1
2
3
4
5
6
7
8
9
2
2
4
4
2
8
1
6
4
a b c d e f g h i j k l m n o p
1
2
3
4
5
6
7
8
9
2
2
4
4
2
8
1
6
4
a b c d e f g h i j k l m n o p
1
2
3
2
0
5
1
4
0
4
8
Test Coverage
3
5
6
7
9
1
2
1. Build Coverage Matrix
2. Select tests that uniquely cover tasks
3. Loop
a. Remove all the tasks covered by selected tests
b. Choose the test that covers most remaining tasks
Regression Suite: 5, 9
Regression Suite: 5, 9, 6

## Slide 44: Greedy Algorithm Example
1
2
3
4
5
6
7
8
9
2
2
4
4
2
8
1
6
4
a b c d e f g h i j k l m n o p
1
2
3
2
0
5
1
4
0
Regression Suite: 5, 9, 6
4
8
Test Coverage
3
5
6
7
9
1
2
1. Build Coverage Matrix
2. Select tests that uniquely cover tasks
3. Loop
a. Remove all the tasks covered by selected tests
b. Choose the test that covers most remaining tasks
1
2
3
4
5
6
7
8
9
2
2
4
4
2
8
1
6
4
a b c d e f g h i j k l m n o p
1
2
3
4
5
6
7
8
9
2
2
4
4
2
8
1
6
4
a b c d e f g h i j k l m n o p
1
2
3
2
0
5
1
4
0
0
1
0
1
0
0
1
2
0
Regression Suite: 5, 9, 6, 8

## Slide 45: When Is Verification Done?
Regress
Coverage
Complete?
Bug Rate
Dropped
No Open
Issues
Review
Clean
Regression
“Ship It”!
Yes
No
No
No
No
No
Yes
Yes
Yes
Yes

## Slide 46: Tape-Out Readiness
Before sending a design to manufacturing, it must meet established tape-out criteria
The criteria is a series of checklists that indicate completion of planned work
Verification is just one element in this series of checklists
Tape-out readiness is measured by a set of metrics
The most relevant metrics for verification are bug rates and coverage

## Slide 47: Escape Analysis

## Slide 48: Escape Analysis
An escape is a bug found later in the verification process then it should have been
  In other words, it escaped its target place
  Usually, escapes refer to bugs found in the hardware itself instead of during simulation
Escape analysis has two important aspects
  Make sure that the bug is fully understood and fixed correctly
    We do not want another tape-out because of a bad fix
  Understand why the bug escaped simulation in the first place and try to improve the verification plan and process to avoid such escapes in the future

## Slide 49: Individual Escape Analysis Timeline
Anomaly found
in hardware
Anomaly determined
to be a functional
problem
Collect data and theorize on
the bug source
Reproduce
the bug in
simulation or
formal verification
Look for
related bugs
Design team
determines fix
Verification team
validates fix
Analyze and
categorize the
escape
Fix applied
to hardware
Time

## Slide 50: How big is Exhaustive?
Consider simulating a typical CPU design
  500k gates, 20k DFFs, 500 inputs
  70 billion sim cycles,
  running on 200 linux boxes for a week
  How big: 236 cycles
Consider formally verifying this design
  Input sequences: cycles 2(inputs+state) = 220500
  What about X’s: 215000 (5,000 X-assignments + 10,000 non-reset DFFs)
  How big: 220500 cycles (215000 combinations of X is not significant here!)
That’s a big number!
  Cycles to simulate the 500k design: 236 (70 billion)
  Cycles to formally verify a 32-bit adder: 264 (18 billion billion)
  Number of stars in universe: 270 (1021)
  Number of atoms in the universe: 2260 (1078)
  Possible X combinations in 500k design: 215000 (104515 x 3)
  Cycles to formally verify the 500k design: 220500 (106171)
Simulasaurus

## Slide 51: Summary
Completion of the Verification Cycle includes:
  Coverage analysis
  Failure analysis
  Regression
  Tape-out readiness
  Escape analysis

## Slide 52: Are We There Yet?

## Slide 53: Why red wine is so important for Christmas
Merry Christmas and a Happy New Year