## Slide 1: COMS31700 Design Verification: Stimuli Generation
Kerstin Eder
(Acknowledgement: Avi Ziv from the IBM Research Labs in Haifa has kindly permitted the re-use of some of his slides.)
Department of
COMPUTER SCIENCE

## Slide 2: Last Time
Coverage
  Code
  Structural
  Functional
Coverage analysis
  Hole analysis
(Discuss plan for coming weeks!)

## Slide 3: Outline
Motivation: Advanced Stimulus Generation
Running example – PowerPC processor
Issues in stimuli generation
  Level of stimuli, test length, etc.
Randomness
Mapping stimuli generation to Constraints and Constraint Satisfaction Problems (CSP)

## Slide 4: Goals of Stimuli Generation
Achieve all the items in the test scenarios matrix of the verification plan
  Ensure that the scenario in the matrix is happening
  Ensure that “bad effects” are propagating to an existing checker
    Hitting a bug without exposing it is worth nothing
But also
  Hitting and exposing all the problems we did not think about in the verification plan
  Provide information about the design and help recreate and understand problems
  Ensure that nothing gets broken over time

## Slide 5: Running Example – PowerPC Processor
Black box view
  Interface to memory (via caches)
    For instruction fetching
    For data fetching and storing
  Interface to I/O devices
    For data fetching and storing
    Interrupts
  Miscellaneous interface
    Clocks
    Reset
    …
PowerPC
Processor
Memory
Instructions
Data
I/O
Clock
Reset

## Slide 6: Architectural View
RISC (Reduced Instruction Set Computer) processor
  “Small” number of instructions (~400)
  One simple operation per instruction
  Fixed length instructions (32 bits = 1 word)
  Specific load and store instructions to access memory
    All other instructions use registers for operands
Large register files
  32 general purpose registers (GPR)
  32 floating-point registers (FPR)
    Used only for floating-point operations
  Several special purpose registers
    Condition register, link register, status register, etc.
Complex memory model
  Multiple level address translation
  Coherency rules
  (not in the scope of the lecture)

## Slide 7: Microarchitectural View
Multi-threaded
In-order execution
Four instructions wide
  Fetch
  Decode
  Dispatch
Four execution units
  B – Branch
  S – Load Store
  R – Simple Arithmetic
  M – Complex Arithmetic
Dispatch
B1
B2
B3
R1
R2
R3
M1
M2
M3
S1
S2
S3
S4f
S4b
Data Fetch
Execute
Write Back
Decode
Fetch
I Cache
D Cache

## Slide 8: Extracts from the Verification Plan
Check that all pairs of instructions are executed correctly together
  Basic architectural requirement
  Appears in most verification plans of processors
  Fulfilling it is not as easy at it seems
Check that all forwarding mechanisms between pipeline stages are working properly
  Basic microarchitectural requirement
  Source for many bugs in previous designs
Check that dispatch queue is not overfilled
  Hard to reach corner case

## Slide 9: Processor Verification Environment
PowerPC
Processor
Instructions
Driver
I/O
Driver
Memory
Driver
Instr
I/O
Data
Instructions
Generator
I/O
Generator
Memory
Generator

## Slide 10: Issues in Stimuli Generation
How many generators?
Level of abstraction
Online vs. offline generation
Dynamic vs. static generation
Test length
Randomness

## Slide 11: How Many Generators?
Distributed generators
  Each interface has its own generator
  Each generator works on its own
  Advantages
    Simple
    Easy to reuse
  Disadvantages
    Hard to reach corner cases in coordinated fashion
PowerPC
Processor
Instr.
Driver
I/O
Driver
Memory Driver
Instr.
Generator
I/O
Generator
Memory Generator

## Slide 12: How Many Generators?
Single generator
  One generator controls all the interfaces
  Advantages
    All the interfaces can work together toward a common goal
  Disadvantages
    Complex
    Hard to reuse
PowerPC
Processor
Instr.
Driver
I/O
Driver
Memory Driver
Unified Generator

## Slide 13: How Many Generators?
Synchronized generators
  Each interface has its own generator
  The generators share information and synchronize
  Advantages
    Can reuse each generator separately
    Can work together towards a common goal
PowerPC
Processor
Instr.
Driver
I/O
Driver
Memory Driver
Instr.
Generator
I/O
Generator
Memory Generator

## Slide 14: Abstraction Level of Generation
DUV
Bit Level
(no abstraction)
Command & Data
instruction level
Groups of bits
Groups of
instructions
Groups of
sequences
across
time
Verification
Level
Designer
System
Program or
Algorithmic Level
Sequence Level

## Slide 15: What Does Abstraction Level Mean?
Communication between:
the user and the generator
    How the user specifies directives to the generator
Internal representation and operation level in the generator
    The level in which the generator generates the stimuli
Communication between:
the generator and the driver
    The generator sends information at high level of abstraction
    The driver translates into bits using the appropriate protocol

## Slide 16: Which Abstraction Level To Choose?
Communication between the user and the generator
  Use level similar to the level of the verification plan
  In our case – the sequence level
Internal representation and operation level in the generator
  Conflicting requirements
    Address user requests (at their level)  high level of abstraction
    Need sufficient detail  low level of abstraction
  In many cases we use two or more levels of generation
    First we build a high-level skeleton of the stimuli based on the user request
    Next we add lower-level details
Communication between the generator and the driver
  Use the lowest level in which the generator operates
  Special case – error injection

## Slide 17: Error Injection
Error detection and recovery are very important mechanisms in hardware designs
  They are also very hard to verify
Error injection is usually done at the lowest level of abstraction
  The value of a bit (or set of bits) is flipped when they are injected into the DUV
To allow error injection, the generator needs to operate and communicate with the driver at the bit level
  This creates extra burden and unnecessarily increases complexity for normal cases
Possible solution – create separate error injection interface between the generator and driver
  At the low level of the error injection
  At the normal level with instructions on how to inject the error

## Slide 18: Online Vs Offline Generation
When to generate stimuli?
Online generation (on-the-fly):
the stimuli generation generates the stimuli during simulation
  The next element is generated when needed by the driver
  The generator must be part of the verification environment
Offline generation (pre-run) – the entire stimuli is generated before the simulation begins
  The generation and simulation can be two separated processes

## Slide 19: Online Generation
Why
  The generator is part of the verification environment
  It can use information about the state of the environment and DUV for improving the quality of generation
    Makes reaching corner cases easier
  The only solution for responders
  Generally small memory footprint
Why not
  Must generate items in order
  Limited complexity

## Slide 20: Offline Generation
Why
  Can separate the generation from simulation
    Use external tools, emulation, …
  Can use more complex algorithms for generation
    For example, generate out of order
  May be compulsory (Where?)
Why not
  Need to integrate generator to the verification environment
  Cannot use information from the DUV and environment
  Hard to create responders

## Slide 21: Generating Out Of Order
Goal – forward data from M2 to B2
  Branch is dispatched after arithmetic instruction
  Both reach stage 2 together
  Branch waits for the arithmetic instruction to complete
Dispatch
B1
B2
B3
M1
M2
M3
Data Fetch
Execute
Write Back
Decode
Generation Order
Lw G10, 60(G21)
Add G7, G9, G13
Mul G1, G2, G3
Div G4, G5, G6
Br 100(G1)
1
3
2
4
4

## Slide 22: Mixing online and offline Generation
Online and offline generation can be mixed within a verification environment
Which designs would benefit from this combination?
  (Example will be discussed in lecture.)

## Slide 23: Dynamic vs. Static Generation
In static generation the generator is not aware of the state of the DUV and the environment
  Generation decisions are based entirely on the internal state of the generator
  Less restrictive definition – the generator is aware of what and when it is allowed to generate
    In calc1 the generator knows not to generate a new command before a response is received
In dynamic generation the generator is fully aware of the state of the DUV and the environment and generates based on this information
  The generator can react to interesting states in the DUV

## Slide 24: Dynamic Generation Example
Goal – forward data from M2 to B2
  The generator identifies potential forwarding condition
  Generates instruction that will block the branch from dispatching with mul
  Generates br instruction with same register to create dependency
Dispatch
B1
B2
B3
M1
M2
M3
Data Fetch
Execute
Write Back
Decode
Next instruction
mul
add
?
?
div
br

## Slide 25: Does This Example Work?
This example may not work!
Main reason:
  The distance from the entry point of instructions to the processor to the dispatch queue
  Many bad things can happen while the br instruction travels this distance
    For example, exceptions that flush the pipes
  By the time it reaches the relevant stage in the pipe, the interesting condition is already gone

## Slide 26: Dynamic Vs. Static Generation
Dynamic generation is based on reaction while static generation is based on planning
In general, reaction is harder than planning
  Time is a factor
  Unexpected events
Most generators use dynamic features lightly
  Observe and react to shallow or stable states and resources
    For example, architectural registers

## Slide 27: Offline Dynamic Generation
Dynamic and static generation should not be confused with online and offline generation
Offline generator can use dynamic generation by using a reference model that provides information about the state of the DUV
  The level and accuracy of the information depends on the abstraction level and accuracy of the reference model

## Slide 28: Test Length
Two extreme approaches for selecting the test length
Use short tests
  The shortest tests that can fulfill the requirement in the verification plan
  For the instruction pairs requirement use tests with just two instructions 
Use long tests
  Combine many requirements in a single test
  Wrap a test with initial and ending sequences

## Slide 29: Why Short Tests?
Easy to create
Easy to debug
Easy to maintain
Short time to simulate

## Slide 30: Why Long Tests?
Need fewer tests
Less time to simulate
  Do not need to repeat initialization sequence for every requirement
Test is not at or near the initial state most of the time
Use less traveled paths
Reach target in more ways
  Often leads to reaching the target in unexpected ways

## Slide 31: Short Vs. Long

## Slide 32: Randomness - Motivation
The first time we press the button a test is created
What happen when we press the button a second time?
  The same test appears  our stimuli generator is deterministic
Stimuli
Generator
Test # 1
Add G1, G2, G3
Mul G6, G9, G11
…
Test # 1
Add G1, G2, G3
Mul G6, G9, G11
…

## Slide 33: Why Deterministic?
(Do not confuse deterministic with manual!)
Useful before random environment is ready
  It is much easier to create a driver that reads deterministic tests and injects them into the DUV
Previously developed test suite
  For example, architectural compliance suite
Known quality
Avoid extremely long generation time

## Slide 34: Why Not Deterministic?
A given test can be used only once
  It is useless unless something has changed in the
    DUV
    Environment
The test specification has limited reuse capabilities
Modern verification methodology employs many workstations that simulate many test cases
  We cannot afford to provide different test specifications for each test case simulated
What about hitting and exposing all the problems we did not think about in the verification plan?

## Slide 35: Random Stimuli Generation
Stimuli
Generator
Test # 1
Add G1, G2, G3
Mul G6, G9, G11
…
Test # 2
Fdiv F1, F2, F3
Lw G6, (10)G9
…
Repeat
100 times
Test
Specification
Test # 3
Fmul F1, F2, F3
Xor G6, G1, G2
…
The generated tests are different !

## Slide 36: Pure Random Generation
The opposite end of the spectrum to deterministic generation
The generator generates random sequences of ‘0’ and ‘1’ that are packed into instructions
Theoretically, this might seem like the ideal solution
  Avoid blind spots in the verification plan
BUT practically,
not very useful for verification
  Most generated test cases are invalid
  Most valid test cases are not
  interesting

## Slide 37: Side Note – Pseudo Random
Random decisions are controlled by a seed
  Given the value of the seed, random decisions are deterministic
  Each random decision updates the value of the seed (in a deterministic fashion)
Pseudo random is essential in verification because of the need to reproduce specific tests
  For example, to reproduce bugs
Requirement for Pseudo Random Test Generator:
  Need (at least) repeatability!
    Achieved by using same seed to seed the generator.

## Slide 38: Constrained Random Generation
The stimuli generator is constrained to generate
  Valid tests
  Tests that meet the user requests
There are many (infinite number of) tests that fulfill these constraints
The generator can choose any such test

## Slide 39: Example – Instruction Pair Generation
The test specification is a test with an add instruction followed by an xor instruction
  Comes from the first extract of the verification plan
The test should look like
Everything else can be randomized
add_xor_test
Start:
…
Add ??, ??, ??
Xor ??, ??, ??
…

## Slide 40: Random Decisions for add_xor_test
Processor operation mode
Start address of the program
Prelude sequence
Epilogue sequence
Registers of add instruction
Data of add instruction
Registers of xor instruction
Data of xor instruction
Behavior of caches, I/O, …
…

## Slide 41: How To Make Random Decisions
Pure random decisions
  Most tests will be invalid
Constrained random decisions
  Limit random decisions to those that lead to valid tests
  Choose uniformly among valid possibilities
  Result
    Generated tests are valid
    Most random decisions are not interesting  Small gain in test quality
“Smart” constrained random decisions
  Bias decision toward interesting cases
  Can lead to significant improvement in test
  quality
Notes: Use example from Marten 

## Slide 42: “Smart” Decisions for add_xor_test
Start address of the program
  Page 0
  Start of page
  Near end of page
Registers of add instruction
  G0
Data of add instruction
  Result = 0
  Overflow
  Long sequences of ‘1’ (long carry chains)
Registers of xor instruction
  Same registers as add instruction

## Slide 43: Smart Decisions
These decisions usually represent generic knowledge of what is interesting in verification
  Add with result 0 is interesting in all addition operations
  Interdependency between registers is interesting in all processors
  G0 is an interesting operand in all PowerPC processors
This collection of knowledge is often called “Testing Knowledge”
The testing knowledge is usually incorporated in the generation environment
  The generation tool you buy
  The generation driver you develop

## Slide 44: Using Testing Knowledge
Testing knowledge is applied automatically to generated stimuli where possible
The generator biases random decisions towards interesting scenarios using the testing knowledge
  Other cases are not shut-down completely to avoid missing cases we never thought about.
Stimuli generators that use testing knowledge are often called “biased random stimuli generators”
Users can change the bias of items in the testing knowledge as part of the test specification
  We will see examples later and can explore how this works when developing the testbench for A2.

## Slide 45: Extracts from the Verification Plan
Check that all pairs of instructions are executed correctly together
  Basic architectural requirement
  Appears in most verification plans of processors
  Fulfilling it is not as easy at it seems
Check that all forwarding mechanisms between pipeline stages are working properly
  Basic microarchitectural requirement
  Source for many bugs in previous designs
Check that dispatch queue is not overfilled
  Hard to reach corner case
Notes: This slides is here purely to remind you of what the verification / test generation targets were when we set out to investigate Stimulus Generation. It is equivalent to slide #8.

## Slide 46: All Instruction Pairs Generation
With biased random stimuli generator we can generate tests that cover all the specific items of the all instruction pairs extract from the verification plan
Every activation of the test specification will produce a new high-quality test suite
For all inst I {
For all inst J {
Generate prelude
Generate I
Generate J
Generate epilogue
}
}
Stimuli
Generator
Test # 1
Add G1, G2, G3
Mul G6, G9, G11
…
Test # 2
Fdiv F1, F2, F3
Lw G6, (10)G9
…
Test # 3
Fmul F1, F2, F3
Xor G6, G1, G2
…

## Slide 47: Forwarding Path Generation
The same approach cannot work for the forwarding path requirement
  There is a difference between the language of the test and the language of the requirement
    The test language is instructions, registers, memory
    The requirement language is microarchitectural events
Three possible solutions
  Manual translation
  Automatic translation
  “Loose” generation

## Slide 48: Manual Translation
The user provides a description of an instruction sequence that creates the event
  For example, mul followed by div followed by br, where br uses same register as target of mul
The generator randomly fills in missing details
  For example, registers and data of div
Suffers from all the disadvantages of manual test creation
  Labor intensive
  Error prone
  Hard to maintain

## Slide 49: Automatic Generation
The generator is aware of the microarchitecture of the processor and knows how to translate a microarchitectural request to a sequence of instructions
  Such generators are often called “Deep Knowledge” test generators
Advantages
  Generated tests cover the requested event with high probability
Disadvantages
  High development cost
  Potentially long generation time
  Sensitive to changes in the design  high maintenance cost

## Slide 50: “Loose” Generation
Rely on the power of massive generation
Use the “normal” test vocabulary to bias the generated tests toward tests that improve the probability of hitting the requested event
  Increase probability of complex arithmetic and branch instructions
  Increase probability of read after write dependency
Coverage is used to ensure that the requested events did occur
Usually, one test specification will be used to cover many items in the verification plan

## Slide 51: Summary: Requirements from Stimuli Generator
Generated stimuli need to be
  Valid
    Behavior of DUV under the test is fully specified
      NOTE: Valid is not necessarily legal
    The verification environment can determine if the DUV behaved correctly
  Interesting
    Improve coverage
    Reach corner cases
    Find bugs
  Meet specific user requirements
    Resource reuse, interdependencies

## Slide 52: Test program constraints
All requirements can be expressed as constraints
add R1  R2 + R3
load Rx  1000 (Ry)
????  ??, Rz
mult Rz  R6 * R7
Quality: sum zero
Validity: x, y
User request: same register

## Slide 53: Constraint Satisfaction Problem Definition
[ Mackworth, Freuder, Montanari, Dechter, Rossi, ...]
CSP P = {V, D, C}
Variables V
  Address
  Register_value
Domains D (finite sets) for each variable
  Address: 0x0000 - 0xFFFF
  Number of bytes in a 'load': { 1, 2, 4, 8, 16 }
Constraints C (relations) over variables
  (load n bytes)  (align address to n bytes boundary)
  value(base_reg) + displacement = address

## Slide 54: Solution for Constraint Satisfaction Problem
Every variable is assigned a value from its domain, such that all constraints are satisfied
  All solutions are born equal.
  There is no better or best solution!
Example
Variables: a, b, c
Domains: A = {1,2,3} ; B = {2,3,4,5} ; C = {1,3,5}
Constraints:
  a2 < b ; c ≠ b ; a < c - 1
(One) Solution:
  a = 1 ; b = 4 ; c = 3

## Slide 55
Random Test Program Generator
Test # 1
Add G1, G2, G3
Mul G6, G9, G11
…
Test # 2
Fdiv F1, F2, F3
Lw G6, (10)G9
…
Repeat
100 times
Test
Specification
Test # 3
Fmul F1, F2, F3
Xor G6, G1, G2
…
CSP Engine
TG Engine
1. Everything included
Putting It All Together: Building a Random Test Program Generator - I

## Slide 56
Random Test Program Generator
Test # 1
Add G1, G2, G3
Mul G6, G9, G11
…
Test # 2
Fdiv F1, F2, F3
Lw G6, (10)G9
…
Repeat
100 times
Test
Specification
Test # 3
Fmul F1, F2, F3
Xor G6, G1, G2
…
CSP Engine
TG Engine
2. External CSP Engine
TK
validity
Putting It All Together: Building a Random Test Program Generator - II

## Slide 57: Putting It All Together: Building a Random Test Program Generator - III
Processor Model
Test # 1
Add G1, G2, G3
Mul G6, G9, G11
…
Test # 2
Fdiv F1, F2, F3
Lw G6, (10)G9
…
Repeat
100 times
Test
Specification
Test # 3
Fmul F1, F2, F3
Xor G6, G1, G2
…
CSP Engine
Random Test Program Generator
3. Model-based test generator
TK
validity

## Slide 58: Model-based Test Generator
Three main layers:
General purpose CSP engine (solver)
  May be specific for stimuli generation, but can be shared among various tools
Processor model
  Description of a specific processor
    Instruction set, registers, memory model, etc.
  Testing knowledge specific to the processor
Processor test generation engine
  Knows about the concept, vocabulary of processors
  Generic testing knowledge of processors
  Can translate the user request, processor model, and testing knowledge into CSP and CSP solution into a test program

## Slide 59: Bug Detection: Dual Attack Approach
Specifying a scenario
Instructions as building blocks
Constrain properties
Inter-instruction relations
Test
Specification
All of
Repeat x3
Repeat x10
FP load /
store
load /
store
Interrupt
Read: 80
Write: 20
The Bug
Intelligent background noise
Built-in testing knowledge
User direction

## Slide 60: Summary: Main Principles of Test Generation
Stimulus generated each cycle using parameter biasing to determine that cycle’s input.
The environment must have the knowledge of legal and illegal scenarios.
Single scenario test cases with some random generation of peripheral inputs.
Random generations used only for inputs not critical to the test case intent.
Single scenario test. Usually written by hand to verify a specific scenario.
Most often early in verification process.
Test case generators using random parameters to bias the stimulus.
Architecturally correct tests are created and then exercised via simulation.
Mainly Biased Pseudo Random (i.e. created using bias control)
Mainly Deterministic
(i.e. written for a specific scenario)
Online Generation (during sim)
Offline Generation (prior to sim)
Notes: This slide allows you to test your knowledge. See whether you would have got these combinations right. ;)