## Slide 1: COMS31700 Design Verification: Verification Cycle, Verification Methodology & Verification Plan
Kerstin Eder
(Acknowledgement: Avi Ziv from the IBM Research Labs in Haifa has kindly permitted the re-use of some of his slides.)
Department of
COMPUTER SCIENCE

## Slide 2: The Verification Cycle

## Slide 3: The Verification Cycle
Functional
Specification
Designer implements
the functional specification
(in HDL)
Create
Verification
Plan
Develop Verification Environment
Stimulus, checkers,
Formal Verification
Debug HDL and
Environment
Run Regression
Perform Escape
Analysis
Debug Fabricated
Hardware
Lessons
Learned
Tape Out
Readiness
Plan
Review

## Slide 4: Functional Specifications
The functional specification describes the desired product
It contains the specification of:
  The function that it must perform.
  The interfaces with which it communicates.
  The conditions that affect the design.
Designers implement the specification in HDL
Verification engineers incorporate the functional specification into the verification plan and environment.
  This may seem redundant, but it is the foundation of verification, i.e. the specification for the verification.

## Slide 5: Create Verification Plan
Functions to be verified: list the functions that will be verified at this level of verification.
  Functions not covered: any functions that must be verified at a different level of the hierarchy.
Resources required (people) and schedule details: tie the plan to the program management by estimating the cost of verification.
Required tools: list the software and hardware necessary to support the described environment.
Specific tests and methods: define the type of environment that the verification engineers will create.
Completion criteria: Define the measurements that indicate that verification is complete.

## Slide 6: Develop Verification Environment
The verification environment is the set of software code and tools that enable the verification engineer to identify flaws in the design.
  The software code tends to be specific to the design,
  while the tools are more generic and are used across multiple verification projects
Major components in the verification environment are stimulus and checking for simulation based environments, and rules generation for formal verification environments
The environment is continually refined throughout the verification cycle
  Refinements include fixes and additions to the software code

## Slide 7: Debug HDL and Environment
Run tests according to the verification plan and look for anomalies
Examine the anomalies to reveal the failure source
  Can be either in the verification environment or in the HDL design
Fix the cause of the failure
  Either the verification environment or the HDL design
Once the problem is fixed, rerun the exact same test
  This aims to ensure that the update corrects the original anomaly and does not introduce new ones
Update the verification plan based on lessons learnt

## Slide 8: Run Regression
Regression is the continuous running of the tests defined in the verification plan
Often, verification teams leverage large workstation pools, or “farms”, to run an ever-increasing number of verification jobs
Regression is used to uncover hard-to-find bugs and ensure that the quality of the design keeps improving
With chip fabrication on the horizon, the verification team must reflect on the environment to ensure that
  they have applied all valid scenarios to the design
  and performed all pertinent checks
  This is the tape-out readiness checkpoint.

## Slide 9: Debug Fabricated Hardware
The design team releases the hardware to the fabrication facility when they meet all fabrication criteria
  This process is also known as the tape-out.
The design team receives the hardware once the chip fabrication completes
The hardware is then mounted on test vehicles or into the planned systems for these chips
The hardware debug team performs the “hardware bring-up”
  During hardware bring-up, further anomalies may present themselves.

## Slide 10: Perform Escape Analysis
Analysis of bugs that were found later than when they should have
The goal is to fully understand the bug, as well as the reasons that it went undiscovered by the verification environments
Important goal: Reproduce the bug in a simulation environment, if possible.
  The lack of reproduction in the verification environment indicates that the design team may not understand the bug
  It would then follow that the team cannot assert that the bug fix is correct without reproducing the original bug in verification.

## Slide 11: Common Verification Breakdowns
Verification based on the design itself instead of the specification
Underdeveloped verification plans
Underdeveloped specifications
Lack of resources
Tape-out based on schedule instead of pre-defined measures

## Slide 12: Summary
Functional verification is a necessary step in the development of today’s complex digital designs
Verification engineers must understand the specification and internal microarchitecture of the design under verification
  They couple this knowledge with programming skills, RTL comprehension, and a detective’s ability to find the scenarios that uncover bugs.
The two main challenges in the verification process:
  Creation of a comprehensive set of stimulus
  Identification of incorrect behavior when encountered
The foundation for a successful verification is the well-defined verification cycle
  The process includes creation of test plans, writing and running verification tests, debugging, and analysis of the holes in the verification environments

## Slide 13: Verification Methodology

## Slide 14: Outline
Verification methodology evolution
Basic verification environment
Evolution of the Verification plan
Contents of the Verification plan
  Functions to be verified
  Specific tests
  Coverage goals
  Test case scenarios (Tests list)
(Calc1 Example)

## Slide 15: Simulation-based Verification Environment Flow
Output
Simulation
Engine
Test case results
Test case
Test case
Driver or
translator
(not always required)
Design
Source
Model
VHDL
Verilog
Environment
Data
Initialization
Run-time requirements

## Slide 16: Simulation-based Verification Environment Structure
DUV
Stimulus
Initiator A
Stimulus
Initiator B
Monitor
Scoreboard
Checker
Stimulus
Responder
This is another (slightly more sopisticated) example of a testbench.
(New components to be covered during the following lectures.)

## Slide 17: Verification Methodology Evolution
Time
Test Patterns
Test Cases
Test Case
Generators
Test Case
Drivers
More Stress per Cycle
Coverage tools
(Formal Verification)

## Slide 18: Test Patterns
Patterns that are created to test specific behaviors
Each pattern handles a single scenario
Tests patterns are hand generated
DUV behavior is manually checked
  For example, by viewing wave forms
Expensive to create
Expensive to maintain
Expensive to execute

## Slide 19: Test Cases
Mostly change the checking of the test
  Stimuli is still hand generated and for a single scenario
Checking evolves to
  Self checking tests
    The test knows at which signals to look and which values should be there
  Automatic checking
    The checking is independent of the stimuli
Automatic checking opens the door for random stimuli
Around this stage the verification profession was born

## Slide 20: Test Case Generators
Replace hand-crafted specific test patterns with machine generated random patterns
  Single scenario → multiple scenarios
  Specific target → more generic targets
  Small number of tests → large number of tests
Test case generators are tools that are external to the verification environment
  Offline generation
  For the environment, tests are hardcoded

## Slide 21: Test Case Drivers
The stimuli generation is embedded in the verification environment
Stimuli are generated during the operation of the environment (and simulation)
The driver can react to the state of the DUV
  Can improve the quality of the stimuli and stress per cycle

## Slide 22: Coverage
The move from target-specific test cases to random stimuli generation reduced the ability of the verification team to ensure that all interesting cases are verified
Coverage measurement and analysis are the “automatic replacement” for this
  Replaces one-to-one matching with many-to-many
    Many tests can potentially hit many interesting cases
Coverage ensures that test cases hit the scenarios they are supposed to hit
  And highlight untested areas
Coverage measures the effectiveness of the verification

## Slide 23: Verification Plan

## Slide 24: Evolution of the Verification Plan
The source of the verification plan is the Functional Spec document
  Must understand the DUV before determining how to verify it
  Confront unclear and ambiguous definitions
  Incomplete and changing continuously
Other factors may affect its content

## Slide 25: Design and Verification Process Interlock
Design Cycle Duration
High Level
Design
Design Implementation
Final Physical
Design
Create
Verification
Plan
Evolve Verification Plan
Implement
Environment
From Plan
Debug HDL and Environment:
Write and Run Tests from Plan
Regression
Functional
Specification
Development
Architects
Designers
Verification Engineers
Initial Review Milestone
Final Review Milestone
Tape Out

## Slide 26: Calc1 Verification Plan
The design description from A1 details the intent of the Calc1 design.
  It is the verification engineer’s job to prove that the actual design implementation matches the intent.
Even for a relatively simple design like Calc1, it is still best not to jump into test case writing before thinking through the entire verification plan requirements.
Please note:
  For the feedback session on A1, please bring your verification plan with you.
  You can obtain feedback on your verification plan until 3 days before the deadline.

## Slide 27: Contents of the Verification Plan
Description of the verification levels
Functions to be verified
Resource requirements
Required tools
Schedule
Specific tests and methods
Coverage requirements
Completion criteria
Test scenarios (Matrix)
Risks and dependencies

## Slide 28: Description of Verification Levels
The first step in building the verification plan is to decide on which levels to perform the verification
The decision is based on many factors, such as
  The complexity of each level
  Resources
  Risk
  Existence of a clean interface and specification
The decision should include which functions are verified at lower levels and which at the current level
Each level and piece selected need to have its own verification plan

## Slide 29: Verification Levels for Calc1
Calc1 is simple enough to be verified only at the top level
  In addition we do not have enough details on the internal components
In more realistic world we may decide to verify the ALU and shifter alone
  For example, using formal verification

## Slide 30: Functions to be verified
This section lists the specific functions of the DUV that the verification team will exercise
  Omitted functions may slip away and not be verified
Assign Priority for each function
  Critical functions
  Secondary functions
Functions not verified at this level
  Fully verified at a lower level
  Not applicable to this level

## Slide 31: Required Tools
Specification and list of the verification toolset
  Simulation engines
  Debuggers
  Verification environment authoring tools
  Formal verification tools
  … and more
For Calc1 A1
  Simulation engine
  Waveform viewer
  Verification environment authoring tool
    Or use the HDL to provide the environment

## Slide 32: Specific Tests and Methods
What type of Verification?
  Black box
  White box
  Grey box
Verification Strategy
  Formal Verification
  Deterministic
  Random based
Abstraction level
  Transactions (packets)
Checking
  Simple I/O checking for data correctness
  Behavioral rules for timing

## Slide 33: Abstraction Levels
DUV
Bit Level
(no abstraction)
Command & Data
“packet” level
Groups of bits
Groups of packets
across time
Groups of
sequences across
time
Verification
Level
Designer
System
Program or
Algorithmic Level
Sequence Level

## Slide 34: Coverage Requirements
Traditionally, coverage is the feedback mechanism that evaluates the quality of the stimuli
  Required in all random-based verification environments
  Some aspects of coverage are directly achieved in deterministic testing
Coverage is defined as events (or scenarios) or families of events that span the functionality and code of the DUV
  The environment has exercised all types of commands and transactions
  The stimulus has created a specific or varying range of data types
  The environment has driven varying degrees of legal concurrent stimulus
Soon: Coverage metrics

## Slide 35: Completion Criteria
Regress
Coverage
Complete?
Bug Rate
Dropped
No Open
Issues
Review
Clean
Regression
“Ship It”!
Yes
No
No
No
No
No
Yes
Yes
Yes
Yes
These might include:
Coverage targets
Target metrics, e.g. bug rate drop
Resolution of open issues
Review
Regression results

## Slide 36: Test Scenarios (Matrix)
Specifies test scenarios that will be used throughout the verification process
  deterministic or random
  Scenarios are connected to items in the coverage requirements
Start with a basic set for the basic functionality
  Add more tests to plug holes in coverage, reach corner cases, etc.
Examples for calc1 design

## Slide 37: Test Scenarios for Calc1: Basic Tests (partial list)
Description | Test #
Check the basic command-response protocol on each of the four ports for each command | 1.1
Check the operation of each command (on each port?) | 1.2
Check overflow and underflow for add and subtract commands | 1.3
Check … | 1.4
NOTE: “Check that X” should be read as “Create a scenario that allows checking X”.
These generic tests should be broken to more specific tests
  Test case 1.1.1.1 : Check the protocol for add command on channel 1
  …
  Test case 1.1.2.4 : Check the protocol for sub command on channel 4

## Slide 38: Test Scenarios for Calc1: Advanced Tests (partial list)
Description | Test # | Topic
For each port, check that each command can be followed by other command without leaving the state of the design dirty | 2.1.1 | Command sequences
For all ports combined, check that each command can be followed by other command without leaving the state of the design dirty (concurrent commands) | 2.1.2 | 
Check that there is fairness among the channels | 2.2 | Fairness
Add two numbers that overflow by 1 | 2.3.1 | Corner cases
Add two numbers that reach the maximum value | 2.3.2 | 
Subtract two numbers that underflow by 1 | 2.3.3 | 
Subtract two equal numbers (result is 0) | 2.3.4 | 
Shift (left and right) 0 places | 2.3.5 | 
Shift completely out (left and right) | 2.3.6 | 
Notes: Think at different levels of abstraction:
9999 + 1
binary representation: add numbers that do or do not use a carry chain in an adder 

## Slide 39: Risks and Risk Management
Complexity of design project
Architecture and microarchitecture closure
Resources
  Not just verification
New tools
Deliveries
  Internal
  External
Dependencies
  Design availability
  Quality of lower levels verification
  Tools and verification IP

## Slide 40: Summary
Verification Cycle
  Foundation for successful verification
Verification Methodology
  Evolution of:
    Test patters
    Test cases
    Test case generators/drivers
Verification Plan
  The specification for the verification process.