## Slide 1: COMS31700 Design Verification: Checking
Kerstin Eder
(Acknowledgement: Avi Ziv from the IBM Research Labs in Haifa has kindly permitted the re-use of some of his slides.)
Department of
COMPUTER SCIENCE

## Slide 2: Checking - Outline
Motivation
Issues in checking
  When to check
  What to check
Checking technologies
  Reference models
  Scoreboards
  (Rule-based checking)
    (Assertions)
Assertion-based verification (ABV) – later 

## Slide 3: The Yin-Yang of Verification
  We cannot find bugs without creating the failing conditions
  We cannot find bugs without detecting the incorrect behavior
Driver
Checker
Driving and checking are the yin and yang of verification

## Slide 4: Ideal Checking
In theory – detect deviation from expected behavior as soon as it happens and where it happens
  No need to worry about “disappearing errors”
  Easy to debug – the checker points to the bug
This is not easy (even if we ignore many practical aspects) because in many cases we understand that something bad happened only in retrospect
  Several “good” behaviors collide to create a bad behavior
And what about the bugs we are not looking for

## Slide 5: “Good” Behavior Collision
At cycle 1000 fdiv F1, F2, F3 is dispatched to the M unit
  It reaches stage M2 at cycle 1001
  Its execution time is 60 cycles
At cycle 1023 fld F1,100(G2) is dispatched to the S unit
  It reaches stage S2 at cycle 1024
The data returns from the cache at cycle 1060
At cycle 1061 the fdiv is ready to write
  It moves to stage M3
At cycle 1061 the fld is ready to write
  It moves to stage S3
Both instruction write to the same
register together
Dispatch
M1
M2
M3
Decode
S1
S2
S3
S4f
S4b

## Slide 6: “Good” Behavior Collision
There are many possible causes for the problem
Notes: This slide encourages you to think about what could cause this problem, e.g. bugs in the detection of R-W dependencies between instructions etc.

## Slide 7: Practical Aspects
Consider:
The cost of implementation and maintenance
  Against the cost of debugging
The cost of mistakes
  Misdetection
    We failed to detect a bug that was exposed by the stimuli.
  False alarm
    We mistakenly flagged a good behavior as bad.
  Which is more expensive?

## Slide 8: When to check

## Slide 9: When to Check?
Checking can be done at various stages of the verification job
  During simulation
    On-the-fly checking
  At the end of simulation
    End-of-test checking
  After the verification job finishes
    External checking
Checking at each stage has its own advantages and disadvantages

## Slide 10: On-the-fly Checking
Checking is done while the simulation is running
The DUV is continuously monitored to detect erroneous behavior
Cycle t+0 t+1 t+2 t+3 t+4 t+5 t+6 t+7 t+8 t+9 t+10 t+11 t+12
clk
duv_inputs
duv_outputs
Check Expected
vs. Actual
Transaction 1
Transaction 2
Transaction 1
Transaction 2
Checker
Stimulus
DUV

## Slide 11: On-the-fly Checking
Advantages
  Detection can be as close as possible (in time and space) to the bug source
  Can stop test as soon as bug occurs; no wasted simulation cycles
  Do not require large traces and external tools to do the checking
Disadvantages
  May slow down simulation
  Checking is limited to allowed time and space complexity
  Need to plan the checking in advance
    To add a new checker, we need to rerun simulation

## Slide 12: End-of-test Checking
Checking is done at the end of simulation
The checker checks the state of internal and external resources and makes sure that they are correct
clk
DUV Instruction
DUV Operands
Internal Resource 1
External Resource 2
Cycle 0 1 2 3 4 5 ………………… t-3 t-2 t-1 t
Instr1
…..
…..
…..
Instr2
Instr3
InstrN
Data1
Data2
Data3
DataN
…..
…..
Checker
Stimulus
Monitor
DUV

## Slide 13: End-of-test Checking
Disadvantages
  Provides limited checking capabilities
    Static look at the state of resources at the end of the test
  High probability of masking bugs by rewriting to the resources
  Hard to detect performance bugs
    Correct things are happening, but not at the right time
  Hard to correlate symptoms to bugs
    Hard to debug
Advantages
  Simpler than other forms
    May not require a deep understanding of the DUV
  Reduces probability of false alarms
    Caused by disappearing bad effects

## Slide 14: External Checking (Monitors)
Monitors keep internal resources values and behaviors in trace files
Checking is done by an external program that examines these files
External
Checker
Program
Stimulus
Monitor
DUV
Actual
Results
clk
duv_inputs
monitor captures internal resource(s)
Cycle 0 1 2 3 4 5 ………………… t-3 t-2 t-1 t
Transaction 1
Transaction N
…..
…..

## Slide 15: External Checking
External checking separates the checking from the simulation
  We can perform any check we want without rerunning the simulation
    As long as the data is in the trace files
  We can perform more complicated checks
    Use longer history, process events out-of-order
  We can combine information coming from different sources
    For example, different verification environments
In theory, external checking has all the powers of on-the-fly checking plus end-of-test checking - plus more
  (Trace size and amount of traced facilities is a practical limitation.)

## Slide 16: What to check

## Slide 17: What to Check
There are five main sources of checkers
  The inputs and outputs of the design (specification)
  The architecture of the design
  The microarchitecture of the design
  The implementation of the design
  The context of the design
    e.g. protocol compliance
Note that the source of checkers and their implementation are two different issues

## Slide 18: Coarser Classification – The What And the How
Add 1+2
3
How
What

## Slide 19: Checking the What
Check the final outcome of a behavior
  Data oriented
    But not limited to data
  Usually based on higher level of abstraction
    Checking is less tight
    Requires less familiarity with the DUV
    Fewer false alarms, more misdetections
  Low correlation between failure and bugs
    Harder for debugging
    Can find “unexpected” bugs

## Slide 20: Checking the How
Check how things are done internally
  Control oriented
  Usually at lower levels of abstraction
    Closer to implementation
  More false alarms, fewer misdetections
  Tighter relations between failure and bugs

## Slide 21: Stimuli Generation and Checking
In general, checking should be isolated from the stimuli generation
  Modularity – ability to replace the stimuli generator
  Reusability – ability to use the checkers at higher level of the design hierarchy
  Independence of Checking from Generation
Exceptions
  Self-checking tests
  Golden vectors
The stimuli generation can assist checking by improving observability
  Help transfer events from dark corners to the spotlight

## Slide 22: Self-Checking Testbenches
Knowledge of the DUV functionality can be built into the TB.
  This automates the checking process.
  Verification engineers encode their knowledge of correct DUV functionality into the checkers, monitors and scoreboard using:
    Golden Vectors,
    Reference Models,
    Protocols or Transactions.
This results in a “self-checking” TB.
  Checkers are “always” active.

## Slide 23: Contemporary TB Architecture

## Slide 24: Contemporary Testbench Architecture
H. Foster: “Response checkers, monitors and asserstions”. In Practical Design Verification by Pradhan and Harris (editors). Cambridge, 2009.
Test Controller
Scoreboard /
Response Checker
Coverage Collector
Slave
DUV
Stimulus Generator
Driver
Responder
Monitor
Monitor
Assertions

## Slide 25: Monitors
Monitors are TB components that observe the inputs, outputs, or internals of the DUV.
  Monitors watch activity of the DUV.
    Black box: DUV inputs and outputs
    Grey box: potentially selected internals
  Monitors can convert low-level signals to transactions.
  Monitors can flag simple timing and protocol errors.
  Monitors collect functional coverage.
  Monitors update the scoreboard.
  Monitors don’t drive DUV pins; they are “passive”.
    Monitors are self-contained and don’t cause “side effects”.
    Monitors are re-usable at different levels of abstraction.
Notes: White box????

## Slide 26: Types of Monitors
Input monitors:
  Collect inputs to the DUV and pass them to scoreboard.
  Can have checker components.
Output monitors:
  Observe the outputs from the DUV and pass them to the scoreboard.
  Can have checker components.
Coverage monitors
  Collects inputs, outputs and selected internal signals.
  Permit analysis of stimulus and functionality coverage.

## Slide 27: Checking Technologies

## Slide 28: Scoreboards
Scoreboards are smart data structures that keep track of events in the DUV during simulation
Usually, scoreboards are global
  One scoreboard per verification environment
Scoreboard are not checking mechanisms, but
  The main purpose of using scoreboards is for checking
  In practice, many checkers are implemented inside scoreboards
  There are many typical checks that are done with scoreboards

## Slide 29: Scoreboard Operation
DUV
Scoreboard
OK?

## Slide 30: Scoreboards Overview
Scoreboards source information from
  the inputs and outputs of the DUV, and
  occasionally also from internal events in the DUV.
Scoreboards are very useful in dataflow designs
    Routers, cache designs, queues
Types of checks enabled using a scoreboard:
  Matching outputs with inputs
    No loss of data
      Detect inputs with no matching output.
    No creation of data
      Detect output with no matching input.
    No unintended modification of data
  Timing specification
    Delay from input to output remains within specified limits.
  Data order

## Slide 31: Scoreboarding in e - 1
Assume: DUV does not change order of packets.
  Hence, first packet on scoreboard has to match received packet.
  import packet_s;
  unit scoreboard {
  !expected_packets : list of packet_s;
  add_packet(p_in : packet_s) is {
  expected_packets.add(p_in);
  };
  check_packet(p_out : packet_s) is {
  var diff : list of string;
  -- Compare physical fields of first packet on scb with p_out.
  -- Report up to 10 differences.
  diff = deep_compare_physical(expected_packets[0], p_out, 10);
  check that (diff.is_empty())
  else dut_error(‘‘Packet not found on scoreboard’’, diff);
  -- If match was successful, continue.
  out(‘‘Found received packet on scoreboard.’’);
  expected_packets.delete(0);
  };
  };

## Slide 32: Scoreboarding in e - 2
Recording a packet on the scoreboard:
  Extend driver such that
  When packet is driven into DUV call add_packet method of scoreboard.
    Current packet is copied to scoreboard.
  It is useful to define an event that indicates when packet is being driven.
Checking for a packet on the scoreboard:
  Extend receiver such that
  When a packet was received from DUV call check_packet.
    Try to find the matching packet on scoreboard.
  It is useful to define an event that indicates when a packet is being received.

## Slide 33: Side Note – Graceful End-of-test
Checking that nothing is lost is very important
If an input does not have a matching output, how can we distinguish between two cases
  The input is lost or hopelessly stuck in the DUV
  The DUV did not have enough time to handle the input
Possible solution – Start a timer when a new input enters the DUV
  If the timer expires, that input is lost or stuck
  But, what if the delay cannot be bound?
Alternative (or complementary) solution – stop the inputs before the end of the test and let the design clean itself
  Because there are no new inputs, things that are stuck inside have a chance to get free

## Slide 34: Reference Models
A reference model is an oracle that tells how the DUV should behave
  Usually in the form of an alternative implementation
It runs in parallel to the DUV, using the same inputs and provides the checking mechanisms with information about the expected behavior
  Checking is done by comparing the expected behavior to the actual one
Pure reference models can run independently of the DUV
  But not all reference models are pure (example later)

## Slide 35: Reference Model Operation
Reference
Model
DUV
=?

## Slide 36: Reference Models
Reference models have many uses
  Checking
  Aids for stimuli generation
  “Smart” BFM – imitate the function of the DUV
  Vehicles for SW development
What can we check with a reference model
  In principal, anything
  In practice it depends on the level of details and accuracy of the reference model
    And how much of its behavior we are willing to expose

## Slide 37: Levels of Abstraction
The level of abstraction in a reference model dictates the type of information we can get out of it for checking
  Functionally accurate models can be used only to check correctness of data, usually at the end of the test or at well defined points in time
    Timing, order, and other checks need other means
  Cycle accurate models can be used for checking all aspects of I/O behavior
  Cycle accurate and latch accurate models can be used also for checking the internal state of the DUV
    The book calls this type of model deep function reference model

## Slide 38: Impure Reference Model
Sometimes it is impossible (or very hard) for the reference model to duplicate significant decisions made by the DUV
Possible solution: Use information from the DUV to assist the reference model!
R
!
!
DUV
Reference Model
?
?
!

## Slide 39: Rule-based Checking
Checks that a set of rules hold in the DUV
Essentially, all checking is rule-based
Something can be
  Value of a register matches value in reference model
  Data in a packet at the DUV output matches data in the input as stored in the scoreboard
  response_out == 0  data_out == 0
Rule-based checking usually refers to the last case
if (not something) then error

## Slide 40: Rule-based Checking
Rules can come from many sources
  All levels of the design process
    Spec, high-level design, implementation
  Behavior of neighboring units
Rules checking can be implemented in many places
  External checking tools
  Various places in the verification environment
    Interface monitors
    Scoreboards
    End-of-test checkers
  In the DUV itself
Rule-based checking that is embedded in the DUV code is called assertions
Lecture on Assertion-Based Verification

## Slide 41: Putting Coverage, Generation and Checking together: The Verification Environment
(With many thanks to Cadence for providing the animations in this section.)

## Slide 42: Traditional Approach: Directed Testing
Redo if design changes
Automation Significant manual effort to write all the tests
Automation Work required to verify each goal was reached
Completeness Poor coverage of non-goal scenarios … especially the cases that you didn’t “think of”
DUT
Verification engineer sets goals and writes directed test for each item in the Verification Plan:
Notes: Point out that the traditional Verif Planning process usually indicates what test cases need to be written; but the underlying reason for said test cases, should be due to design analysis. Usually the classical test plan will then just document what directed tests need to be written. The test plan should be the set of Goals to achieve, but most plans document the means by which to achieve those goals.
Since manual testing is tedious and labor-prone, the typical method of copy-pasting snippets in test cases results in relatively low variability from 1 test case to the next.

## Slide 43: Directed Test Environment
stimulus
stimulus
stimulus
stimulus
stimulus
stimulus
stimulus
stimulus
stimulus
check
check
check
check
check
check
check
check
check
cov
cov
cov
cov
cov
cov
cov
cov
…
cov
1
2
3
4
5
6
7
8
n
Directed test approach
driver
DUT
slave
directed tests
Composition of a directed test
  Directed tests contain more than just stimulus.
  Checks are embedded into the tests to verify correct behavior.
  The passing of each test is the indicator that a functionality has been exercised.
Reusability and maintenance
  Tests can become quite complex and difficult to understand the intent of what functionality is being verified
  Since the checking is distributed throughout the test suite, it is a lot of maintenance to keep checks updated
  It is usually difficult or impossible to reuse the tests across projects or from module to system level
The more tests you have the more effort is required to develop and maintain them
maint
maint
maint
maint
maint
maint
maint
maint
maint

## Slide 44: Coverage Driven Verification Methodology: Defining Coverage “Goals” Enables Automation
Focuses on reaching goal areas (versus execution of test lists):
Constrained-random stimulus generation explores goal areas (& beyond)
Coverage shows which goals have been exercised and which need attention
(Self-Checking ensures proper DUT response.)
Automation – Constrained-random stimulus accelerates hitting coverage goals and exposing bugs. Coverage and checking results indicate effectiveness of each simulation, which enables scaling many parallel runs.
Even for non-goal states!
DUT
Simply changing seeds generates new stimulus
Add constraints to target a specific corner case

## Slide 45: Coverage Driven Environment
sequencer
scoreboard
transaction
transaction
monitor
monitor
stimulus
Composition of a coverage driven environment
  Reusable stimulus sequences developed with “constrained random” generation
  Running unique seeds allows the environment to exercise different functionality
  Monitors independently watch the environment
  Independent checks ensure correct behavior.
  Independent coverage points indicate which functionality has been exercised.
driver
DUT
slave
0x223F
stimulus
0XA30E
0X94D7
0XFF78
0X3767
0XCC18
0XDA83
0XBA1F
0X95FB
0X382E
stimulus
stimulus
stimulus
stimulus
stimulus
stimulus
stimulus
stimulus
stimulus
seed
new test
coverage collection
check
check
cov
cov
stimulus sequences
stimulus sequences
stimulus sequences
stimulus sequences
sequence
library

## Slide 46: Summary
Coverage Driven Verification Methodology
Driver
Checker
Stimuli Generation
Coverage and
Checking