## Slide 1: COMS31700 Design Verification: Verification Tools Directed Testing with Manual Checking
Department of
COMPUTER SCIENCE
Kerstin Eder
Design Automation and Verification
(Acknowledgement: Avi Ziv from the IBM Research Labs in Haifa has kindly permitted the re-use of some of his slides.)
Notes: Use the spare time at the end to introduce A1.
Explain spec and how to raise questions.
Explain that the TB needs to be modular.
Explain that a plan is required.
Detail the submission: bugreport.txt and structure.pdf
Point out that the TB needs to be generic enough to find bugs in a 2nd version of the design, i.e. if I was to replace the DUV with the one from last year, would your TB still find bugs?

## Slide 2: Functional Verification Approaches
Verification
Reviews
Dynamic
Static
Prototyping
Simulation
Formal
Code
Analysis
Dynamic Formal
Linters
Theorem
Proving
Property
Checking
Equivalence
Checking
Silicon
FPGA
Emulation
Notes: Point out that Equivalence Checking is the most common form of Formal Verification now routinely used in practice.
Point out that it should not be confused with Property Checking.
Point out that Property Checking is also called Model Checking.

## Slide 3: Achieving Automation
Task of Verification Engineer:
Ensure product does not contain bugs - as fast and as cost-effective as possible.
(... and of Verification Team Leader):
  Select/Provide appropriate tools.
  Select a verification team.
  Decide when cost of finding next bug violates law of diminishing returns.
Parallelism, Abstraction and Automation can reduce the duration of verification. (Automation is currently the least applicable!)
Automation reduces human factor, improves efficiency and reliability.
Verification TOOLS are used to achieve automation.
  Tool providers: Electronic Design Automation (EDA) industry

## Slide 4: Tools used for Verification
Dynamic Verification:
  Hardware Verification Languages (HVL)
  Testbench automation
  Test generators
  Coverage collection and analysis
  General purpose HDL Simulators
    Event-driven simulation
    Cycle-based simulation (improved performance)
    Waveform viewers (for debug)
  Hardware accelerators/emulators, FPGAs
Static Analysis / Verification Methods (Formal Methods):
  Linting Tools
  Equivalence checkers
  Model checkers
    Property Specification Languages (ABV)
  Theorem provers
Administration:
  Version Control and Issue Tracking
  Metrics
  Data Management and Data Mining related to Metrics
Third Party Models

## Slide 5: Linting Tools
Linters are static checkers.
Assist in finding common coding mistakes
  Linters exist for software and also for hardware.
    gcc -Wall (When do you use this?)
Only identify certain classes of problems
  Many false negatives are reported.
  Use a filter program to reduce false negatives.
    Careful - don’t filter true negatives though!
Does assist in enforcing coding guidelines!
Rules for coding guidelines can be added to linter.

## Slide 6: Simulation-Based Verification
Directed testing with manual checking

## Slide 7: Fundamentals of Simulation-based Verification
Driver
Checker
How do I know when I’m done?
Verification can be divided into two separate tasks
  Driving the design - Controllability
  Checking its behavior - Observability
Basic questions a verification engineer must ask
  Am I driving all possible input scenarios?
  How will I know when a failure has occurred?
Driving and checking are the yin and yang of verification
  We cannot find bugs without creating the failing conditions
    Drivers
  We cannot find bugs without detecting the incorrect behavior
    Checkers

## Slide 8: What is a Testbench?
“Code used to create a predetermined input sequence to a design, and to then observe the response.”
  Generic term used differently across the industry.
  Always refers to a test case/scenario.
  Traditionally, a testbench refers to code written in a Hardware Description Language (VHDL, Verilog) at the top level of the design hierarchy.
  A testbench is a “completely closed” system:
    No inputs or outputs.
    Effectively a model of the universe as far as the design is concerned.
Testbench
Driver
Checker
DUV
      collect the response and check
      drive stimulus into the DUV
Bugs in the TB
Bugs in DUV
Notes: Do we need reference models and monitors etc here? Probably not for “Directed Testing”.

## Slide 9: Simulation-based Design Verification
Simulate the design (not the implementation) before fabrication.
Simulating the design relies on simplifications:
  Functional correctness/accuracy can be a problem.
Verification Challenge: ”What input patterns to supply to the Design Under Verification (DUV) ...”
Simulation requires stimulus. It is dynamic, not just static!
Requires to reproduce environment in which design will be used.
  Testbench (Remember: Verification vs Testing!)
Verification Challenge: ”... and knowing what is expected at the output for a properly working design.”
Simulation outputs are checked externally against design intent (specification)
  Errors cannot be proven not to exist!
  “Testing shows the presence, not the absence of bugs.”
  [Edsger W. Dijkstra]
Two types of simulators: event-based and cycle-based

## Slide 10: General HDL Simulators
Most Popular Simulators in Industry
  Mentor Graphics ModelSim/Questa
  Cadence NCSim
  Synopsys VCS
Support for full language coverage
  "EVENT DRIVEN" algorithms
VHDL's execution model is defined in detail in the IEEE LRM (Language Reference Manual)
Verilog's execution model is defined by Cadence's Verilog-XL simulator ("reference implementation")

## Slide 11: Simulation based on Compiled Code
To simulate with ModelSim:
  Compile HDL source code into a library.
  Compiled design can be simulated.
Write HDL code
Compile HDL code
Simulate the design
HDL files
HDL library
Compile
Simulate
Correct syntax errors
Debug the design

## Slide 12: Event Flow Example
Inputs
Outputs
Block B
Block C
B1
B2
C1
C2
C3
D
s1
s2
s3
s4
s5
s6
1
2
3
4
5
i1
i2
i3
i4
s7
s9
s10
s11
s12
s13
s8

## Slide 13: Event-based Simulators
Event-based simulators are driven based on events. 
Outputs are a function of inputs:
  The outputs change only when the inputs do.
  The event is the input changing.
  An event causes the simulator to re-evaluate and calculate new output.
Outputs (of one block) may be used as inputs (of another) ...
Re-evaluation happens until no more changes propagate through the design.
Zero delay cycles are called delta cycles!

## Slide 14: Delta Cycles
Event propagation may cause new values being assigned after zero delays.
  (Remember, this is only a model of the physical circuit.)
Although simulation time does not advance, the simulation makes progress.
NOTE: Simulation progress is first along the zero/delta-time axis and then along the simulation time axis.
Delta Time
Simulation Time
event
It is possible to write models that unintentionally get stuck in
delta cycles!

## Slide 15: Event Driven Principles
The event simulator maintains many lists:
  A list of all atomic executable blocks
  Fanout lists: A data structure that represents the interconnect of the blocks via signals
  A time queue – points in time when events happen
  Event queues – one queue pair for each entry in the time queue
    Signal update queue
    Computation queue
The simulator needs to process all these queues at simulation time.

## Slide 16: Core Algorithm of an Event-Driven Simulation Engine
Activate next
scheduled block
More Blocks
Scheduled?
Perform Signal Updates
1
2
3
Scheduling Data
Block/Signal Interconnect Topology
Event Data
no
yes
yes
More Blocks
Scheduled?
no
Increment
Model Time?
Done
Block Code
Block Function Execution
Schedule Signal Updates
call
return

## Slide 17: Simulation Speed
What is holding us back?
Speedup strategies

## Slide 18: Improving Simulation Speed
The most obvious bottle-neck for functional verification is simulation throughput
There are several ways to improve throughput
  Parallelization
  Compiler optimization techniques
  Changing the level of abstraction
  Methodology-based subsets of HDL
    Cycle-based simulation
  Special simulation machines

## Slide 19: Parallelization
Efficient parallel simulation algorithms are hard to develop
  Much parallel event-driven simulation research
  Has not yielded a breakthrough
  Hard to compete against "trivial parallelization"
Simple solution – run independent testcases on separate machines
  Workstation "SimFarms"
  100s - 1000s of engineer's workstations run simulation in the background

## Slide 20: Compiler Optimization Techniques
Treat sequential code constructs like general programming language
All optimizations for language compilers apply:
  Data/control-flow analysis
  Global optimizations
  Local optimizations (loop unrolling, constant propagation)
  Register allocation
  Pipeline optimizations
  etc.
Global optimizations are limited because of model-build turn-around time requirements
  Example: modern microprocessor is designed with ~1Million lines of HDL
    Imagine the compile time for a C-program with ~1M lines!

## Slide 21: Changing the Level of Abstraction
Common theme:
  Cut down the number of scheduled events
  Create larger sections of un-interrupted sequential code
  Use less fine-grained model structure
    Smaller number of schedulable blocks
  Use higher-level operators
  Use zero-delay wherever possible
Data abstractions
  Use binary over multi-value bit values
  Use word-level operations over bit-level operations

## Slide 22: Changing the Level of Abstraction
process (a, b)
begin
s(2 to 0) <= ('0' & a (1 to 0)) + ('0' & b(1 to 0) );
sum_out(1 to 0) <= s(1 to 0);
carry_out <= s(2);
end process
s(0) <= a(0) xor b(0);
c(0) <= a(0) and b(0);
s(1) <= a(1) xor b(1) xor c(0);
c(1) <= (a(1) and b(1)) or (b(1) and c(0)) or (c(0) and a(1));
sum_out(1 to 0) <= s(1 to 0);
carry_out <= c(1);
s(2 to 0) <= ('0' & a (1 to 0)) + ('0' & b(1 to 0) );
sum_out(1 to 0) <= s(1 to 0);
carry_out <= s(2);

## Slide 23: Changing the Level of Abstraction
Scheduling the small blocks
  {A1, B1, A2, B2, A3, B3, A4, B4}
  Each small block is executed once
Scheduling the big blocks
  {A, B, A, B, A, B, A, B}
  A = A1 and A2 and A3 and A4
  Each small block is executed 4 times
A
B
A1
A2
A3
A4
B1
B2
B3
B4

## Slide 24: Changing the Level of Abstraction
Model granularity
Number of blocks
Performance
Many tiny blocks:
High scheduling overhead
Few large blocks:
High re-scheduling overhead
Decreasing
Model Activity Rate

## Slide 25: Synchronous Design Methodology
The design is comprised of
  State-holding (storage) elements
  Combinational logic for state transition function
State-Holding
Elements
Clock(s)
State Transition Function
(Combinational
Logic)
Primary inputs
Primary
outputs

## Slide 26: Cycle Based Model Build Flow
Language compile – synthesis-like process
  Simpler because of missing physical constraints
  Logic mapped to a non-cyclic network of Boolean functions
  Hierarchy is preserved
Flatten hierarchy – crush design hierarchy to increase optimization potential
Optimization – minimize the size of the model to increase simulation performance
Levelize logic
Translate to instructions

## Slide 27: Model Build – Levelization
Levelized
Combinational Logic
Latches
A
B
C
Logic is ordered into levels so that
order of evaluation is correct.
E.g., A and B are computed before C.

## Slide 28: Translate to Instructions
and
a
b
and
xor
s(0)
c(0)
xor
xor
=>
s(1)
sum_out(1)
and
and
or
or
=>
=>
sum_out(0)
carry_out
c(1)
1
Load temp1, a(0)
Load temp2, b(0)
Xor temp1, temp2, temp3
Store temp3, s(0)
And temp1, temp2, temp3
Store temp3, c(0)
Load temp1, a(1)
Load temp2, b(1)
Xor temp1, temp2, temp3
…
We can convert every Boolean function into a minimal set (~4 or better) of instructions
1
2
3
1
2
3

## Slide 29: Parallelism in Generated Code Cycle-Sim
Word-level operations can be easily parallelized
  Is translated into
A(0 to 31) <= B(0 to 31) and C(0 to 31) and D(0 to 31)
LoadWord R1, B(0 to 31)
LoadWord R2, C(0 to 31)
AND R1, R1, R2
LoadWord R2, D(0 to 31)
AND R1, R1, R2
StoreWord R1, A(0 to 31)

## Slide 30: Synchronous Design Methodology
Clock the design only so fast as the longest possible combinational delay path settles before cycle is over
Cycle time depends on the longest topological path
  Hazards/Races do not disturb function
  Longest topological path can be analytically calculated w/o using simulation -> stronger result w/o sim patterns
and
xor
xor
and
and
or
or
clock : dependent on critical path

## Slide 31: Hardware Acceleration
Programs created for cycle simulation are very simple
  Small set of instructions
  Simple control – no branches, loops, functions
Operations at the same level can be executed in parallel
Hardware acceleration uses these facts for fast simulation by utilizing
  Very large number of small and simple special-purpose processors
  Efficient communication and scheduling

## Slide 32: Scheduling Example
b
a
e
c
d
g
i
f
h
j
k
l
EP4 | EP3 | EP2 | EP1 | 
c | d | a | b | Step1
e |  | f | g | Step2
 |  | h | i | Step3
 |  |  | k | Step4
 |  | l | j | Step5
12 steps serial, 5 steps parallel

## Slide 33: Accelerator Basic Structure
Notes: Logic Processing units = LPs
These are special purpose processing units, so they are faster than CPUs. 

## Slide 34: Principle of Operation
Compiler transforms combinational logic into Boolean operations
Compiler schedules interprocessor communications using a fast broadcast technique
Emulation performance dictated by
  Number of processors
  Number of levels in the design

## Slide 35: Simulation Speed Comparison
Event Simulator
1
Cycle Simulator
20
Event driven cycle Simulator
50
Acceleration
1000
Emulation
100000

## Slide 36: Verification Languages
Raising the level of abstraction

## Slide 37: Verification Languages
Need to be designed to address verification principles.
Deficiencies in RTL languages (HDLs such as Verilog and VHDL):
  Verilog was designed with focus on describing low-level hardware structures.
    No support for data structures (records, linked lists, etc).
    Not object/aspect-oriented.
      Useful when several team members develop testbenches.
  VHDL was designed for large design teams.
Limitations inhibit efficient implementation of verification strategy.
High-level verification languages are (currently):
  System Verilog
    IEEE 1800 [2005] Standard for System Verilog- Unified Hardware Design, Specification, and Verification Language
  e-language used for Cadence’s Specman Elite [IEEE P1647]
  (Synopsys’ Vera, System C)

## Slide 38: Features of High-Level Verification Languages
Raising the level of abstraction:
  From bits/vectors to high-level data types/structures
    lists, structs, scoreboards including ready made functions to access these
Support for building the verification environment
  Enable testbench automation
  Modularity
    Object/aspect oriented languages
    Libraries (VIP) to enable re-use
Support for test generation
  Constrained random test generation features
    Control over randomization to achieve the target values
    Advanced: Connection to DUV to generate stimulus depending on DUV state
Support for coverage
  Language constructs to implement functional coverage models

## Slide 39: Any other *verification* Languages?
Tommy Kelly, CEO of Verilab:
“Above all else, the Ideal Verification Engineer will know how to construct software.”
Toolkit contains not only Verilog, VHDL, SystemVerilog and e, but also Python, Lisp, mySQL, Java, ... 

## Slide 40: Directed Testing
Focus on checking

## Slide 41: The Importance of Driving and Checking
Drivers activate the bug.
The observable effects of the bug then need to propagate to a checker.
A checker needs to be in place to detect the incorrect behaviour.
All three are needed to find bugs!
Activation
Propagation
Detection

## Slide 42: Checking: How to predict expected results
Methods for checking:
  Directed testing:
    Because we know what will be driven, a checker can be developed for each test case individually.
Sources for checking:
  Understanding of the inputs, outputs and the transfer function of the DUV.
  Understanding of the design context.
  Understanding of the internal structures and algorithms (uarch).
  Understanding of the top-level design description (arch).
  Understanding of the specification.
Beware:
  Often, all outputs of the design must be checked at every clock cycle!
    However, if the outputs are not specified clock-cycle for clock-cycle, then verification should not be done clock-cycle for clock cycle!
  Response verification should not enforce, expect, nor rely on an output being produced at a specific clock cycle.

## Slide 43: Limitations of Using Waveform Viewers as Checkers
Often come as part of a simulator.
Most common verification tools used...
  Used to visually inspect design/testbench/verification environment.
  Recording waves decreases performance of simulator. (Why?)
Don’t use viewer to determine if DUV passes/fails a test.
  Why not?
Can use waveform viewer for debugging.
  Consider costs and alternatives.
  Benefits of automation.
  Need to increase productivity.

## Slide 44: Limitations of Directed Testing: Coverage
Criteria:
Effectiveness
Efficiency
Maintainability
Re-usability
Coverage
Time
100%
Directed Approach
Constrained Pseudo-random Coverage Driven Approach
Need to increase productivity!
Directed testing has many shortfalls wrt these criteria.
Why would one use Directed Testing?
Notes: Typical bug finding curve using only directed tests? (How would it look like?)
What does Coverage mean?
  Need to find bugs early
  Why use Directed Testing? [to sanity check whether the TB works – before using random generation ;) or for coverage closure]

## Slide 45: Impact of Increasing Verification Productivity
Time
Total
Number
of Bugs
found
Test
Verification
Productivity improvements drive
early problem discovery
Need to find bugs early

## Slide 46: Verification Tools
Third Party Models
Metrics

## Slide 47: Third Party Models
Chip needs to be verified in its target environment.
  Board/SoC Verification
Do you develop or purchase behavioural models (specs) for board parts?
  Buying them may seem expensive!
  Ask yourself:
  “If it was not worth designing on your own to begin with, why is writing your own model now justified?”
  The model you develop is not as reliable as the one you buy.
  The one you buy is used by many others - not just yourself.
Remember: In practice, it is often more expensive to develop your own model to the same degree of confidence than licensing one.

## Slide 48: Metrics
Not really verification tools - but managers love metrics and measurements!
  Managers often have little time to personally assess progress.
  They want something measurable.
Coverage is one metric - will be introduced later.
Others metrics include:
  Number of lines of code
  Ratio of lines of code
  (between design and verifier)
  Drop of source code changes
  Number of outstanding issues

## Slide 49: Summary
We have covered:
Verification Tools & Languages
Basic testbench components
Writing directed tests
The importance of Driving and Checking
Checking when we use directed testing
Limitations of directed testing
Cost of debug using waveforms