## Slide 1: COMS31700 Design Verification: Assertion-based Verification
Kerstin Eder
(Acknowledgement: Avi Ziv from the IBM Research Labs in Haifa has kindly permitted the re-use of some of his slides.)
Department of
COMPUTER SCIENCE

## Slide 2: What is an assertion?
An assertion is a statement that a particular property is required to be true.
  A property is a Boolean-valued expression, e.g. in SystemVerilog.
Assertions can be checked either during simulation or using a formal property checker.
Assertions have been used in SW design for a long time.
  assert() function is part of C #include <assert.h>
  Used to detect NULL pointers, out-of-range data, ensure loop invariants, etc.
Revolution through Foster & Bening’s OVL for Verilog.
  Clever way of encoding re-usable assertion library in Verilog. 
  Assertions have become very popular for Design Verification in recent years: Assertion-Based Verification (also Assertion-Based Design).
Notes: Have a look at OVL, e.g. always and never. How are they defined in Verilog – see how simple they are? The uptake of assertions in HW verification is very much due to the provision of OVL, which reduced the encoding of properties to using a set of well documented easy to understand macros (OVL modules). So, designers no longer needed to think about how to write the properties they wanted to express, but just about which macro to use and what the “test expression” to enter into the macro call should be. 

## Slide 3: HW Assertions
HW assertions:
combinatorial (i.e. “zero-time”) conditions that ensure functional correctness
  must be valid at all times
    “This buffer never overflows.”
    “This register always holds a single-digit value.”
    “The state machine is one hot.”
    “There are no x’s on the bus when the data is valid.”
and
temporal conditions
  to verify sequential functional behaviour over a period of time
    “The grant signal must be asserted for a single clock cycle.”
    “A request must always be followed by a grant or an abort within 5 clock cycles.”
  Temporal assertion languages facilitate specification of temporal properties.
    System Verilog Assertions
    PSL/Sugar

## Slide 4: Who writes the assertions?
DUV
System
Architects
Verification Engineers
IP Providers
Standards
Designers
Notes: Discussion on “Who writes the assertions?”
Architects
Designers
Verification Engineers
IP Providers
Standards
Lead discussion towards different types of assertions: implementation (design) and specification (intent) assertions

## Slide 5: Types of Assertions

## Slide 6: Types of Assertions: Implementation Assertions
  Also called “design” assertions.
  Specified by the designer.
  Encode designer’s assumptions.
    Interface assertions
      Catch different interpretations between different designers.
  Formulate conditions of design misuse or design faults:
    detect buffer over/under flow
    signal read & write at the same time when only one is allowed
Implementation assertions can detect discrepancies between design assumptions and implementation.
But implementation assertions won’t detect discrepancies between functional intent and design! (Remember: Verification Independence!)

## Slide 7: Types of Assertions: Specification Assertions
  Also called “intent” assertions
    Often high-level properties.
  Specified by architects, verification engineers, IP providers, standards.
  Encode expectations of the design based on understanding of functional intent.
  Provide a “functional error detection” mechanism.
  Supplement error detection performed by self-checking testbenches.
    Instead of using (implementing) a monitor and checker, in some cases writing a block-level assertion can be much simpler.

## Slide 8: Safety Properties
Safety: Something bad does not happen
  The FIFO does not overflow.
  The system does not allow more than one process to use a shared device simultaneously.
  Requests are answered within 5 cycles.
More formally: A safety property is a property for which any path violating the property has a finite prefix such that every extension of the prefix violates the property.
[Accellera PSL-1.1 2004]
Safety properties can be falsified by a finite simulation run.
Notes: This is good news, i.e. if a safety property is violated, we can find out based on a finite simulation run.

## Slide 9: Liveness Properties
Liveness: Something good eventually happens
  The system eventually terminates.
  Every request is eventually acknowledged.
More formally: A liveness property is a property for which any finite path can be extended to a path satisfying the property. [Foster etal.: Assertion-Based Design. 2nd Edition, Kluwer, 2010.]
In theory, liveness properties can only be falsified by an infinite simulation run.
  Practically, we often assume that the “graceful end-of-test” represents infinite time.
    If the good thing did not happen after this period, we assume that it will never happen, and thus the property is falsified.
Notes: Note: SVA does not have the eventually operator. PSL does: “!”.
This is bad news! It means that we can’t tell whether a liveness property is violated just by looking at a finite trace – any such trace could be turned into a passing trace (i.e. a trace where the property is satisfied) in the future. 
Example: The traffic light eventually turns green. If you stand at the light for x seconds and it has not turned green and may decide to give up, concluding it never will. But, just as you walk away, it may turn green. You just did not wait long enough. However, we can’t tell whether it will turn green eventually or not, if it has not yet done so and we don’t know how long to wait. So, we based on a finite trace we can’t tell a good design (one where the lights eventually turn green) from a bad design (one where the lights never turn green), if we have not yet seen the good behaviour – it could occur at any time.
Discuss how to turn liveness into safety properties by introducing large but finite bounds, e.g. the end of simulation.

## Slide 10: Use of Assertions
Properties describe facts about a design.
Properties can be used to write
  Statements about the expected behaviour of the design and its interfaces
    Combinatorial and sequential
    (Can be used for simulation-based or for formal verification.)
  Checkers that are active during simulation
    e.g. protocol checkers
  Constraints that define legal stimulus for simulation
  Assumptions made for formal verification
  Functional coverage points
Remember to re-use existing assertions, property libraries or checks embedded in VIP.

## Slide 11: How Assertions work during Simulation
Temporal properties can be in one of 4 states during simulation:
  inactive (no match), active, pass or fail
  property req_followed_by_ack; @(posedge clk){ $rose (req) |=> ##[0:1] ack }
  end property
  p_req_ack: assert property req_followed_by_ack;
clk
req
ack
active
active
active
pass
pass
active
fail
fail
Notes: There are two forms of implication: overlapped using operator |->, and non-overlapped using operator |=>.
For overlapped implication, if there is a match for the antecedent sequence expression, then the first element of the consequent sequence expression is evaluated on the same clock tick.
In the example above, if the sequence s1 matches, then sequence s2 must also match. If sequence s1 does not match, then the result is true.

## Slide 12: Overcoming the Observability Problem
If a design property is violated during simulation, then the DUV fails to operate according to the original design intent.
BUT:
Symptoms of low-level bugs are often not easy to observe/detect.
Activation of a faulty statement may not be enough for the bug to propagate to an observable output.
Assertion-Based Verification:
During simulation assertions are continuously monitored.
The assertion immediately fires when it is violated and in the area of the design where it occurs.
Debugging and fixing an assertion failure is much more efficient than tracing back the cause of a failure.

## Slide 13: Example FIFO DUV

## Slide 14: Example DUV Specification - Inputs
Inputs:
  wr indicates valid data is driven on the data_in bus
  data_in is the data to be pushed into the DUV
  rd pops the next data item from the DUV in the next cycle
  clear resets the DUV
DUV
clk
clear
wr
data_in [7:0]
rd
data_out [7:0]
empty
full
data_out_valid

## Slide 15: Example DUV Specification - Outputs
Outputs:
  data_out_valid indicates that valid data is driven on the data_out bus
  data_out is the data item requested from the DUV
  empty indicates that the DUV is empty
  full indicates that the DUV is full
DUV
clk
clear
wr
data_in [7:0]
rd
data_out [7:0]
empty
full
data_out_valid

## Slide 16: DUV Specification
High-Level functional specification of DUV
  The design is a FIFO.
  Reading and writing can be done in the same cycle.
  Data becomes valid for reading one cycle after it is written.
  No data is returned for a read when the DUV is empty.
  Clearing takes one cycle.
  During clearing read and write are disabled.
  Inputs arriving during a clear are ignored.
  The FIFO is 8 entries deep.
Notes: This SPEC is incomplete. It lacks the statement: Data written to a full DUV will be dropped.

## Slide 17: Identifying Properties for the FIFO block
Black box view:
  Empty and full are never asserted together.
  After clear the FIFO is empty.
  After writing 8 data items the FIFO is full.
  Data items are moving through the FIFO unchanged in terms of data content and in terms of data order.
  No data is duplicated.
  No data is lost.
  data_out_valid only for valid data, i.e. no x’s in data.
An invariant property.
Notes:   Behavioural black box properties
  Implementation-specific white box properties
  Discuss options for encoding properties in terms of abstraction levels and observability and implications for ease of bug finding

## Slide 18: Identifying Properties for the FIFO block
White box view:
  The value range of the read and write pointers is between 0 and 7.
  The data_counter ranges from 0 to 8.
  The data in the FIFO is not changed during a clear.
  For each valid read the read pointer is incremented.
  For each valid write the write pointer is incremented.
  Data is written only to the slot indicated by nxt_wr.
  Data is read only from the slot indicated by nxt_rd.
  When reading and writing in the same cycle the data_counter remains unchanged.
    What about a RW from an empty/full FIFO?
Notes:   Behavioural black box properties
  Implementation-specific white box properties
  Discuss options for encoding properties in terms of abstraction levels and observability and implications for ease of bug finding

## Slide 19: Property Formalization
Property Formalization Languages
  Most commonly used languages:
    SVA and
    PSL [IEEE – 1850]
  Assertions can be combinatorial
  property mutex;
  { !(empty & full) }
  end property
  or temporal
  property req_followed_by_ack; @(posedge clk){ $rose (req) |=> ##[0:1] ack }
  end property
Boolean expression
Temporal expression in form of an implication
main condition
(consequent)
pre-condition
(antecedent)
Notes: (Doulos SV course gives good examples of basic intro to SVA)
Potentially, only mention PSL but focus on SVA because we will use SVA for the labs

## Slide 20: Introduction to Writing Properties using SVA
Sequences
  Cycle delay and repetition
Implications
$rose, $fell, $past, $stable
To formalize basic properties using SVA we need to learn about:

## Slide 21: Sequences
Useful to specify complex temporal relationships.
Constructing sequences:
  A Boolean expression is the simplest sequence.
  ## concatenates two sequences.
  ##N cycle delay operator - advances time by N clock cycles.
    a ##3 b b is true 3 clock cycles after a
  ##[N:M] specifies a range.
    a ##[0:3] b b is true 0,1,2 or 3 clock cycles after a
  [*N] consecutive repetition operator
    A sequence or expression that is consecutively repeated with one cycle delay between each repetition.
    a [*2] exactly two repetitions of a in consecutive clock cycles
  [*N:M] consecutive repetition with a specified range
    a[*1:3] covers a, a ##1 a or a ##1 a ##1 a
Notes: Should $ be introduced here?
$ can be used as a maximum value within a repetition
in simulation $ is interpreted as the end of simulation
formal verification tools interpret $ as infinity
SVA does not have the eventually operator. PSL does: “!”.

## Slide 22: Implications
Properties typically take the form of an implication.
SVA has two implication operators:
|=> represents logical implication
  A|=>B is equivalent to (not A) or B,
  where B is sampled one cycle after A.
  req_gnt: assert property ( req |=> gnt );
clk
req
gnt
pass
fail
fail
req_gnt true
non-overlapping implication
Notes: Note, the property is defined from the point where req is true, so in the 1st rising clock, the entire property is true because at the first clock rise it is true that req is followed by gnt in the next clock cycle – hence, the tick. The following two ticks are because req is false, so the implication is trivially true. However, in the clock cycle after (the 4th rise of the clock, the property is not true; this is because the req is true and the grant is not true one cycle after – so no tick under that req as the property fails.
Note the difference between the state a property is in during simulation, i.e. inactive, active, pass, fail, and what the property evaluates to (true or false).

## Slide 23: Implications
SVA has another implication operator:
|-> represents logical implication
  A|->B is equivalent to (not A) or B,
  where B is sampled in the same cycle as A.
  req_gnt_v1: assert property ( req |=> gnt );
  req_gnt_v2: assert property ( req |-> ##1 gnt );
Both properties above are specifying the same functional behaviour.
The overlapping implication operator |-> specifies behaviour in the same clock cycle as the one in which the LHS is evaluated.
Delay operator ##N delays by N cycles, where N is a positive integer including 0.

## Slide 24: Useful SystemVerilog Functions for Property Specification
$rose and $fell
  Compares value of its operand in the current cycle with the value this operand had in the previous cycle.
$rose
  Detects a transition to 1 (true)
$fell
  Detects a transition to 0 (false)
Example:
  assert property ( $rose(req) |=> $rose(gnt) );

## Slide 25: Useful SystemVerilog Functions for Property Specification
$past(expr)
  Returns the value of expr in the previous cycle.
  Example:
  assert property ( gnt |-> $past(req) );
$past(expr, N)
  Returns the value of expr N cycles ago.
$stable(expr)
  Returns true when the previous value of expr is the same as the current value of expr.
  Represents: $past(expr) == expr

## Slide 26: Property Formalization

## Slide 27: Formalization of key DUV Assertions
  System Verilog Assertion for:
    Empty and full are never asserted together.
      property not_empty_and_full;
      @(posedge clk) !(empty && full);
      endproperty
      mutex : assert property (not_empty_and_full);
Is this a safety or a liveness property? Why?
This label is useful for debug.

## Slide 28: Formalization of key DUV Assertions
Alternative encoding: $onehot0 returns true when zero or one bit of a multi-bit expression is high.
  System Verilog Assertion for:
    Empty and full are never asserted together.
      property not_empty_and_full;
      @(posedge clk) $onehot0({empty,full});
      endproperty
      mutex : assert property (not_empty_and_full);
This is a safety property!

## Slide 29: Formalization of key DUV Assertions
Beware of property bugs! Know your operators:
seq1 |-> seq2, seq2 starts in last cycle of seq1 (overlap)
seq1 |=> seq2, seq2 starts in first cycle after seq1
We need: @(posedge clk) (clear |=> empty);
  System Verilog Assertion for:
    After clear the FIFO is empty.
      property empty_after_clear;
      @(posedge clk) (clear |-> empty);
      endproperty
      a_empty_after_clear : assert property (empty_after_clear);

## Slide 30: Formalization of key DUV Assertions
  System Verilog Assertion for:
    On empty after one write the FIFO is no longer empty.
      property not_empty_after_write_on_empty;
      @ (posedge clk) (empty && wr |=> !empty);
      endproperty
      a_not_empty_after_write_on_empty : assert property (not_empty_after_write_on_empty);
    Assertions can be monitored during simulation.
    Assertions can also be used for formal property checking.
    Challenge:
    There are many more interesting assertions.

## Slide 31: Corner Case Properties
FIFO empty: When the FIFO is empty and there is a write at the same time as a read (from empty), then the read should be ignored.
    property empty_write_ignore_read;
    @(posedge clk)(empty && wr && rd |=>
    data_counter == $past(data_counter)+1);
    endproperty
    a_cc1 : assert property (empty_write_ignore_read);
FIFO full: When the FIFO is full and there is a read at the same time as a write, then the write (to full) should be ignored.
      property full_read_ignore_write
      @ (posedge clk) {full && rd && wr |=>
      data_counter == $past(data_counter)-1};
      endproperty
      a_cc2: assert property (full_read_ignore_write);
Notes: Discuss the different ways in which the property can be expressed:
How can we detect that rd/wr has been ignored?
Should we use black or white box properties?
Different levels of observability

## Slide 32: All my assertions pass – what does this mean?
Remember, simulation can only show the presence of bugs, but never prove their absence!
An assertion has never “fired” - what does this mean?
  Does not necessarily mean that it can’t be violated!
    Unless simulation is exhaustive...,
    which in practice it never will be.
  It might not have fired because it was never active.
  Most assertions have the form of implications.
  Implications are satisfied when the antecedent is false!
    These are vacuous passes.
    We need to know how often the property passes non-vacuously!
How do you know your assertions are correctly expressing what you intended?
Notes: Importance of Assertion Coverage
What does it mean that an assertion was never violated?
How do you know assertions are correct?
How do you know assertions are triggered?
Discuss methods to ensure assertions express what you intended: review, mutation, introduce a but and check they fired, etc.

## Slide 33: Assertion Coverage
Measures how often an assertion condition has been evaluated.
  Many simulators count only non-vacuous passes.
  Option to add assertion coverage points using:
  assert property ( (sel1 || sel2) |=> ack );
  cover property ( sel1 || sel2 );
  Coverage can also be collected on sub-expressions:
  cover property ( sel1 );
  cover property ( sel2 );
Notes: Importance of Assertion Coverage
What does it mean that an assertion was never violated?
How do you know assertions are correct?
How do you know assertions are triggered?

## Slide 34: Costs and benefits of ABV
Costs include:
  Simulation speed
  Writing the assertions
  Maintaining the assertions
Benefits include:
  Explicit expression of designer intent and specification requirements
    Specification errors can be identified earlier
    Design intent is captured more formally
  Enables finding more bugs faster
  Improved localisation of errors for debug
  Promote measurement of functional coverage
  Improved qualification of test suite based on assertion coverage
  Facilitate uptake of formal verification tools
  Re-use of formal properties throughout design life cycle
Intellectual step of property capture forces you to think earlier!

## Slide 35: Do assertions really work?
  Assertions are able to detect a significant percentage of design failures:
Assertions should be an integral part of a verification methodology.
[Foster etal.: Assertion-Based Design. 2nd Edition, Kluwer, 2010.]

## Slide 36: ABV Methodology
Use assertions as a method of documenting the exact intent of the specification, high-level design, and implementation
Include assertions as part of the design review to ensure that the intent is correctly understood and implemented
Write assertions when writing the RTL code
  The benefits of adding assertions at later stage are much lower
Assertions should be added whenever new functionality is added to the design to assert correctness
Keep properties and sequences simple
  Build complex assertions out of simple, short assertions/sequences

## Slide 37: Summary
In ABV we have covered:
What is an assertion?
Use and types of assertions
Safety and Liveness properties
Introduction to basics of SVA as a property formalization language
Importance of Assertion Coverage
Costs vs benefits of using assertions