## Slide 1: SoC Verification
Mike Benjamin
Associate at TVS
Notes: Title should ideally be changed to “High Level Testing” – done [KIE]

## Slide 2: What is SoC level?
Top level Looking at the complete design
System Level Putting the complete design in a wider context …
System architecture
Partner IP
Software
Notes: Which of these are ‘high level’ and why?

## Slide 3: What does a simple SoC look like?
7-stages
Integer pipeline
3-Port Register File
Debug Support Unit
Interrupt Controller
AMB AHB Master (32 bit)
Trace Buffer
Debug Support
Interrupt Port
IEEE-754 FPU
Co-Processor
HW Mul/Div
Local I-RAM
I-Cache
Local D-RAM
AHB Master I/F
D-Cache
Interconnects
IP
Peripherals  register map
Memory  memory map
Debug
support
Reset
Clocks
Interrupts
‘Infrastructure’:
CPU
Notes: Top level is simply a real SoC

## Slide 4: Why write SoC level tests?
Some top level functionality not visible at unit level
Allows verification to focus on actual use model
Missing system level functionality & compliance testing
Imported IP
Signal connectivity
Register / address mapping
Power on / reset
Power management
Clocking strategy
Performance verification
Benchmarking
Coherence?
Configurability / parameterized blocks instantiated!
Testing restricted to real use model
Generate typical/worst case waveforms for power analysis!
Partner IP
Software
System architecture
Notes: We’ve already done unit level, isn’t that enough?
Some top level functionality not visible at unit level may also mean more easily visible at top level
Clocking strategy: dynamically changing clock ratios, gated clocks …
Remind people of the difference between verification and validation

## Slide 5: Why bother doing unit level testing?
Controllability at top level v unit level?
 REDUCED
Visibility at top level v unit level?
 REDUCED
Overhead on testing at top level v unit level?
 INCREASED
Harder to hit corner case and longer run times
Harder to debug fails
Need to propagate block level fixes/changes to top level before they can be tested
Need to understand the complete SoC to test and debug a single block
Need working top level integration before testing
Notes: Controllability and visibility reduced at top level
Project timescales increased

## Slide 6: Barriers to top level testing
Barriers to top level verification?
Solutions?
Complexity of building the complete top level design
Late availability of key blocks / functionality
Size of full top level design
Limited controllability of the design from outside
Limited visibility inside design
Difficulty of anyone understanding the complete design
S1:
S2:
S3:
S4:
S5:
S6:
B1:
B2:
B3:
B4:
B5:
B6:
  Require changes to be co-ordinated between dependent blocks
  A schedule defining milestones for delivering features
  Regression testing before changes are committed
  Ensure major interfaces are stable and well defined
  Black box some components
  Replace components with abstract models or BFMs (eg: CPU, memories)
Notes: Small changes / errors in one block can break the complete design
Renaming / changes to hierarchy can break verification tools
Aim to have an always working top level (talk about time boxing incremental delivieries)
Verification objectives of stability and well specified interfaces conflicts with design focus on PPA and timing optimization
Architectural tests are not implementation specific

## Slide 7: Reuse from unit level?
VIP
  BFMs
  Monitors and scoreboards
  Protocol checkers
Assertions
Functional coverage points
Tests
  Integration tests
    Connectivity, address mapping
  Stress tests
    Cross cutting concerns such as interrupts or power management
    Shared resources or ‘convergence points’ (eg: memory synchronisation)
  Right level of abstraction
    Transactions and/or bus accesses
    Relative address map
Need to plan for reuse!

## Slide 8: What do our top level tests contain?
Halt mechanism
main(){
report_start();
leon3_test(1, 0x80000200, 0);
irqtest(0x80000200);
gptimer_test(0x80000300, 8);
gpio_test(0x80000700);
report_end();}
int gpio_test(int addr)
{
pio = (int *) addr;
int mask;
int width;
report_device(0x0101a000);
pio[3] = 0; pio[2] = 0; pio[1] = 0;
pio[2] = 0xFFFFFFFF;
/* determine port width and mask */
mask = 0; width = 0;
while( ((pio[2] >> width) & 1) && (width <= 32)) {
mask = mask | (1 << width);
width++;}
pio[2] = mask;
if( (pio[0] & mask) != 0) fail(1);
pio[1] = 0x89ABCDEF;
if( (pio[0] & mask) != (0x89ABCDEF & mask)) fail(2);
pio[2] = 0;
return width;}
Trace and error reporting
Interrupt handling
Result checking
Register / address map
Component tests
Tests are typically C programs running on an SoC CPU
Loaded into SoC memory

## Slide 9: How to check the test results
Fail causes test to hang
Dump results to memory and compare to reference results from model
  mpeg decoder video stream
  reference simulator
Explicit checks in the test
  Observe and count interrupts
  Check data values
Trace comparison
  Compare simulation state to a reference model cycle by cycle during the simulation
Use of monitors, scoreboards or assertions
Sensitive to accuracy of reference model (especially timing)
Need error propagated to end of test

## Slide 10: Methodology for top level testing
Pipe cleaning flow with regression tests  to verify basic functionality is not broken
Incremental test set verifying the subsets of functionality  scope grows with successive builds
Architectural and conformance tests
Micro-architectual tests
Soak testing
Performance testing and benchmarking
Notes: Architectural tests are not implementation specific

## Slide 11: Adding Coverage
Instruction Set Simulator (ISS)
Coverage
Database
Tests
Parse & Decode
Coverage Base Classes
(ISA view of resources)
Coverage Grids
Execution
Trace
Coverage Model
Why add coverage?
Conformance testing:
  Need complete coverage of cases
Targeting specific scenarios:
  Hitting required corner cases
Soak testing
  Ensure testing is not becoming repetitive
Notes: Why have coverage
Complete coverage of cases for conformance testing
Scenario targeting correct space when doing constrained random
Continuing to generate interesting tests rather than becoming repetitive when doing soak testing

## Slide 12: How to further increase the ‘stress’
Build multiple configurations (set at build time)
  Increase stress by maximising corner cases eg: small memories or FIFOs
  Increase stress my maximising ‘synchronisation points’ eg: shared resources or coherent memories
Chicken bits (set at start of test)
  Turn features on or off (can be verification specific or used to minimise design risk by disabling potentially risky optimisations)
Hot load (set at start of test)
  Can force states of part of the design into conditions that maximise chance of hitting corner conditions early (most often hot load caches but can also leave holes or create dirty entries)
Use of irritators (set during test)
  Hardware/DMA data transfers/traffic generators and BFMs (bursts of traffic and corner cases for transaction timing)
Notes: Transaction timing should include very fast and very slow transactions

## Slide 13: The New Verification Challenges of Low Power Design
Why does low power matter?
  Battery life eg: mobile devices
  Operating temperature and cooling requirements eg: automotive, data centres
How to achieve low power?
  Dynamic power = switching flops
  Static power = leakage current
Minimize Switching by Design
  Clock gating: Inferred (by synthesis) and architectural
Turn off units (eg: run fast then stop)
  Multiple power domains and power modes managed by a ‘Power Management Unit’ (PMU)
  System level (eg: ARM big.LITTLE architecture)
Some of the new Verification challenges
  Ensure correct state retention and restoration when switching a power domain.
  Clamping inactive signals at the boundary of a power domain
  Ensure the design doesn’t try to use a unit that is (being) switched off!
  Can the design get stuck in a power mode?
  eg: interacting state machines restored to states that cause deadlock or livelock
  Errors in the sequences of save and restore operations performed by the PMU
  Interaction of the power modes with chip level power on, off and reset!
Energy efficiency
Power dissipation
Turn off!
Minimise switching

## Slide 14: Power Aware Simulation
Need to tell your RTL simulations about low power intent
    A common description shared between simulation, synthesis and layout
Two competing standards: UPF and CPF
  Both extend the functional description without changing the existing RTL
What they describe…
  Power domains, supply rails and switches eg:
    create_power_domain pdA –include_scope moduleA
    Create_supply_net RETENTION –domain pdA
  State retention and isolation
  System power states
    … the number of state combintions can be large!
For an RTL simulation ‘OFF’ means
  All ‘OFF’ registers are corrupted
  Any signals driven by logic that is ‘OFF’ are corrupted
  No evaluation of logic that is ‘OFF’
Can also describe other features…
  Multi-voltage designs and level shifters
  Voltage and frequency scaling
Retention registers have separate supplies
Isolation cells have separate supplies

## Slide 15: Cost of bugs over time (revisited)
Time
Cost of
bugs
Initial Design Chip System Customer
Number of
bugs found
How do you decided when you are done?
How do you find the remaining bugs?
Notes: You’ve run out of steam?

## Slide 16: Being pro-active to improve verification
Achieving the best possible test plan
  Methodical analysis of design specifications and extraction of features
  Brainstorming and reviewing within the development team
  Refinement and maintenance throughout the development process
  Tracking and sign-off of verification deliverables against the test plan
Make the design ‘verification friendly’ (design for verification) (High quality products are a combination of robust and extensive verification with good design practices)
  Ensure good visibility of architectural and micro-architectural corner cases
  Avoid unnecessary functional complexity eg: excessive configurability, irregular structures
  Understand the verification impact of design changes (eg: code churn during optimization)
  Designers document their intent and assumptions, especially at interface between units
  Ensure the architecture, specifications and design are as stable as possible
Communicate! (Verification is not just the responsibility of verification Engineers)
  Engage closely with the designers
  Be an active participant in reviews
  Take every opportunity to get the widest possible input into verification planning
Verification Requirements Specification

## Slide 17: Is block and top level verification sufficient?
Is block level and top level verification sufficient?
  Verification of IP in System context
  Verifying correct operation with related IP
  Verification of complete systems (both HW and SW)
    Software conformance testing
    Soak testing
Soak testing at system level?
  Focus at system level is shared resources
    eg: coherent memory system
  Running irritator software in parallel on multiple threads or multiple CPUs (minimal OS)
  Switching CPUs (eg: swapping big/LITTLE)
  Virtualisation

## Slide 18: What goes wrong at system level?
Integration bugs
  Connecting a big-endian subsystem to a little-endian sub-system
Clocks and power
  System hangs following mode change
Concurrency and shared resources
  Concurrent memory gets corrupted
Performance
  Bus bandwidth and latency is much worse than predicted

## Slide 19: How to go faster! Compute Farm, Emulators, FPGA and test chips

## Slide 20: The ‘tradeoffs’ for different platforms
 | Compute farm | Emulator | FPGA | Test chip
Speed | 10Hz - 100Hz …per machine | 1MHz | 2MHz – 50MHz | GHz
Observability | Total | Trace window + host debug | Probes + host debug | Host debug
Behavioural testbench? | Yes | Co-emulation (speed penalty) | Co-emulation (speed penalty) | No
Test in ‘real world’ systems | No | Host debug + ICE with speed bridges | Mostly | Yes
Are fails easily reproducible in simulation? | Yes | Yes | No | No
Bring-up time | Minutes | Weeks  hours | Weeks  Days | Months
Partitioning!
Favours lots of short tests!
Depends on process maturity
Complex timing dependencies
… but also need to load tests and dump test results!
Notes: Partitioning usually means multiplexing signals between FPGAs hence speed reduction
Even if you have a compute farm it doesn’t speed up debugging a long test fail!
Importance of early pipe cleaning to develop process maturity

## Slide 21: Summary
What is SoC level verification? (Top v System)
Looked at structure of a simple SoC
Why do both ‘SoC level’ & ’unit level’ verification?
A methodology for SoC level verification
System level verification
If time permits ….
RIS (Random Instruction Stream) Test Generators
Looked at IP-XACT

## Slide 22: Top Level Test Generation
Bias tests to hit interesting corner cases
  Scenario interleaving
  Target shared resources/’points of convergence’
Non-repetitive useful tests
There should be an efficient workflow
  Generation performance
  Target diverse platforms
  Ease of use
  Maintainability
  Reuse (of testing knowledge)
  Effective result checking:
    Propagation of results
    Trace comparison
Testbench
SoC
CPU
A
Mem.
B
C
FABRIC
FABRIC
BFM
BFM
Scenario
Test
Compiler flow
Observe results
Test
generator
Coverage
Expected
results

## Slide 23: ‘Point solutions’ for test generation Memory Coherence
Time sharing a resource (memory)
  Coherency
  Memory protection
Most interesting cases are overlapping accesses
Colliding access can be: Write||Write, Write||Read, Read|| Read eg: PowerPC: ‘store quadword’ || ‘load quadword’
True sharing: same memory
False sharing: close enough to interfere (eg: same cache line)
MP memory model can have weak ordering (with barriers) (W(a,d1) || W(a,d2))  M(a) = {d1, d2}
thread 2
CPU A thread 1
CPU B
fabric
Exclusive CPU B
Shared
Unchecked
Exclusive CPU A, thread 1

## Slide 24: A general purpose test generator for CPUs
Constraints (relations between attributes)
eg: source.address = base.data+displacement.data
PageCross(source.address)
  hard or soft?
Typically several weakly coupled constraints
Randomize all other parameters and events eg: cache event in parallel with load
Huge domains (eg: 2^64 address and data)
Randomly sample solution space
As resources are ‘used up’ it can become harder to solve constraints. Solutions are:
  Register reloading
  Backtrack and retry
Generating loops is a challenge:
  Procedure calls
  Recurring interrupts
  Self modifying code
   Prevent random re-entrant code
Memory access instruction type
Load word
Base register
Offset
Source
Target
register
Test generator
Architectural description
Architecture specific knowledge
Constraint solver
Architecture
independent
knowledge
Test template
Test program
Reference
Simulator
Modelling Engineer
Verification Engineer
Notes: How does test generator know how to construct a valid test?
A: A test is a sequence of instructions

## Slide 25: Model Based Test Generation for SoCs?
Provides ‘system level’ abstraction
Aids modelling testing knowledge
Test case language
Clear separation between system modelling and test description
  eg: different SMP clusters will have same interactions and components and only the configuration will change
Expects a separate checking mechanism
XGEN
Component types
Configuration
Interactions
Testing knowledge
Test request
Test case
Abstract test
Generation Engine
Refinement
Ports with properties (eg: address, access size)
Internal state defined by resources (eg: registers, memory, …)
Behaviour defined by constraints between port properties and internal state
Instantiates components, defines connections, sets static component characteristics eg: address map
Sequence of transactions possibly involving several components
eg: a collision mechanism that biases test cases towards reuse of certain system resources
Notes: A framework providing right level of abstractions whilst hiding complex implementation detail
In principle could build such a framework in SystemVerilog…

## Slide 26: IP-XACT
IP-XACT is:
A standard XML scheme for describing components and connections.
It describes things like interfaces (<spirit:busInterfaces>) and registers (<spirit:memoryMaps>) rather than function!
Tools can then generate and manipulate the metadata:
Packagers: Generate ‘sound’ meta data for components
Generators: Configure components where IP blocks and the design may both have generic parameters
Assemblers & SoC design tools: Create an IP-XACT description of the design that can be used to automatically stitch together the components
Why is it useful to have a standard for documenting IP?
Vendor neutral: exchange libraries and combine components from multiple sources
Allows automation of SoC and test bench assembly … a manual process is very error prone as number of components increases!
Provides a common specification that can be shared between: SoC design, verification, software and documentation teams

## Slide 27: IP-XACT example: IP register description
reserved
Field
‘full’
Field
‘empty’
Access
Read/Write or Read Only?
Width
31
Field offset
1
0
Name
STATUS FLAGS
Address
Ox03
Reset value Ox01
spirit:access
spirit:size
spirit:address offset
spirit:reset
spirit:value
spirit:mask
spirit:field
spirit:bitWidth
spirit:bitOffset
enumeratedValues
Value | Name
0 | NOT_FULL
1 | FULL
Notes: Register Description
Register Fields

## Slide 28: IP-XACT example: Code
<spirit:register>
<spirit:name> STATUS_FLAGS</spirit:name>
<spirit:description> Register contains flags to report if FIFO empty or full </spirit:description>
<spirit:dim>1</spirit:dim>
<spirit:size>32</spirit:size>
<spirit:access>read-write</spirit:access>
<spirit:reset>
<spirit:value>1</spirit:value>
<spirit:mask>3</spirit:mask>
</spirit:reset>
<spirit:field>
<spirit:name>EMPTY</spirit:name>
<spirit:description>FIFO empty flag</spirit:description>
<spirit:bitOffset>0</spirit:bitOffset>
<spirit:bitWidth>1</spirit:bitwidth>
<spirit:access>read-only</spirit:access>
</spirit:field>
<spirit:field>
<spirit:name>FULL</spirit:name>
<spirit:description>FIFO full flag</spirit:description>
<spirit:bitOffset>1</spirit:bitOffset>
<spirit:bitWidth>1</spirit:bitwidth>
<spirit:access>read-only</spirit:access>
</spirit:field>
</spirit:register>