## Slide 1: COMS31700 Design Verification: Block-level Case Study with demonstration of (ABV and) Formal Verification
Kerstin Eder
(Acknowledgement: I gratefully acknowledge the support from Cadence who provide the licenses for the Formal Verification Tool demonstration. Special thanks also to Anton Klotz from the Cadence Academic Network.)
Department of
COMPUTER SCIENCE

## Slide 2: Case Study
Specification Verification Plan Directed Testing (Code Coverage) Functional Coverage Assertion-based Verification Formal Property Checking

## Slide 3: Case Study: FIFO DUV
Remember that the FIFO DUV is part of a larger unit which in turn is part of a larger system.
The demo is focused on the verification of the FIFO at block level only.
data_in [7:0]
wr
rd
clear
clk
full
empty
data_out [7:0]
data_out_valid
FIFO DUV
FIFO DUV
FIFO DUV

## Slide 4: Specification

## Slide 5: Example DUV Specification - Inputs
Inputs:
  wr indicates valid data is driven on the data_in bus
  data_in is the data to be pushed into the DUV
  rd pops the next data item from the DUV in the next cycle
  clear resets the DUV
DUV
clk
clear
wr
data_in [7:0]
rd
data_out [7:0]
empty
full
data_out_valid

## Slide 6: Example DUV Specification - Outputs
Outputs:
  data_out_valid indicates that valid data is driven on the data_out bus
  data_out is the data item requested from the DUV
  empty indicates that the DUV is empty
  full indicates that the DUV is full
DUV
clk
clear
wr
data_in [7:0]
rd
data_out [7:0]
empty
full
data_out_valid

## Slide 7: DUV Specification
High-Level functional specification of DUV
  The design is a FIFO.
  Reading and writing can be done in the same cycle.
  Data becomes valid for reading one cycle after it is written.
  No data is returned for a read when the DUV is empty.
  Clearing takes one cycle.
  During clearing read and write are disabled.
  Inputs arriving during a clear are ignored.
  The FIFO is 8 entries deep.
Notes: This SPEC is incomplete. It lacks the statement: Data written to a full DUV will be dropped.

## Slide 8: Verification Plan
Those who fail to plan, plan to fail.

## Slide 9: The Verification Plan
Functions to be verified:
  For each level in the design hierarchy, list all the functions that will be verified at that level.
  In particular, identify corner cases for the design.
Methods of verification:
  Define which verification methods to use, e.g. simulation (directed or random), formal, etc.
Completion criteria:
  Define the measurements/metrics that indicate that verification is complete.
  In particular, define coverage models and targets.
Resources required (people) and schedule details:
  Integrate the verification plan into the overall design plan and estimate the cost of verification.
Required tools:
  List the software and hardware necessary to perform verification.

## Slide 10: The Verification Plan
Functions to be verified:
  For each level in the design hierarchy, list all the functions that will be verified at that level.
  In particular, identify corner cases for the design.
Methods of verification:
  Define which verification methods to use, e.g. simulation (directed or random), formal, etc.
Completion criteria:
  Define the measurements that indicate that verification is complete.
  In particular, define coverage models and targets.
Resources required (people) and schedule details:
  Integrate the verification plan into the overall design plan and estimate the cost of verification.
Required tools:
  List the software and hardware necessary to perform verification.
The Verification Plan is the Specification
for the Verification Process
Verification Plans are “live” documents.
They change as our understanding of the DUV increases.

## Slide 11: Test Scenarios Matrix - Basic
Description | Test #
Check the write functionality | 1.1
Check the read functionality | 1.2
Check the reset functionality | 1.3
Check … | 1.4
NOTE: “Check that X” should be read as “Create a scenario that allows checking X”.
These generic tests should be broken to more specific tests
  Test case 1.1.1: Check write when empty
  Test case 1.1.2: Check write when full
  Test case 1.1.3: Check write during reset
  …
Develop a Test Scenarios Matrix for our Case Study DUV.

## Slide 12: White Box View DUV Implementation

## Slide 13: Example DUV Implementation
Implementation based on a circular buffer
  nxt_wr and nxt_rd pointers indicate where the next entry will be written to or read from.
  data_counter indicates the number of valid data items in the FIFO.
  Complex control logic for pointers and counter.
nxt_wr
nxt_rd
data_counter

## Slide 14: Functional Coverage

## Slide 15: Cross-Product Functional Coverage
[O Lachish, E Marcus, S Ur and A Ziv. Hole Analysis for Functional Coverage Data. In proceedings of the 2002 Design Automation Conference (DAC), June 10-14, 2002, New Orleans, US.]
A cross-product coverage model is composed of the following parts:
  A semantic description of the model (story)
  A list of the attributes mentioned in the story
  A set of all the possible values for each attribute (the attribute value domains)
  A list of restrictions on the legal combinations in the cross-product of attribute values

## Slide 16: FIFO Cross Product Coverage Model
From a “White Box” verification perspective:
  The FIFO is implemented using a circular buffer.
  The circular buffer implementation is based on the following control signals:
    nxt_rd, nxt_wr, data_counter
  These signals are used to control the data flow and also the empty and full signals.
  Verification Plan:
    “Interactions of read and write transactions can create complex and unexpected conditions. All combinations need to be verified to gain confidence in the correctness of the FIFO.”
This is the story.

## Slide 17: FIFO Cross Product Coverage Model
Attributes relevant to the coverage model:
  nxt_rd, nxt_wr, data_counter, empty, full signals
Attribute value domains:
  nxt_rd ϵ {0,1,2,3,4,5,6,7}
  nxt_wr ϵ {0,1,2,3,4,5,6,7}
  data_counter ϵ {0,1,2,3,4,5,6,7,8}
  empty ϵ {0,1}
  full ϵ {0,1}
Full coverage space:
  8*8*9*2*2 = 2304 coverage tasks
  Format: (nxt_rd, nxt_wr, data_counter, empty, full)
  Find some legal and some illegal examples

## Slide 18: FIFO Cross Product Coverage Model
Attributes relevant to the coverage model:
  nxt_rd, nxt_wr, data_counter, empty, full signals
Attribute value domains:
  nxt_rd ϵ {0,1,2,3,4,5,6,7}
  nxt_wr ϵ {0,1,2,3,4,5,6,7}
  data_counter ϵ {0,1,2,3,4,5,6,7,8}
  empty ϵ {0,1}
  full ϵ {0,1}
Full coverage space:
  8*8*9*2*2 = 2304 coverage tasks
  Format: (nxt_rd, nxt_wr, data_counter, empty, full)
  Find some legal and some illegal examples

## Slide 19: FIFO Cross Product Coverage Model
Attributes relevant to the coverage model:
  nxt_rd, nxt_wr, data_counter, empty, full signals
Attribute value domains:
  nxt_rd ϵ {0,1,2,3,4,5,6,7}
  nxt_wr ϵ {0,1,2,3,4,5,6,7}
  data_counter ϵ {0,1,2,3,4,5,6,7,8}
  empty ϵ {0,1}
  full ϵ {0,1}
Full coverage space:
  8*8*9*2*2 = 2304 coverage tasks
  Format: (nxt_rd, nxt_wr, data_counter, empty, full)
  Find some legal and some illegal examples
Legal Coverage Tasks:
(0,0,0,1,0)
(2,2,8,0,1)
(3,7,4,0,0)
Illegal Coverage Tasks:
(0,0,0,1,1)
(1,1,4,0,0)
(1,5,0,1,1)

## Slide 20: FIFO Cross Product Coverage Model
Restrictions
  data_counter is only important when nxt_rd==nxt_wr so that one can tell the difference between empty and full
  64 combinations of nxt_rd and nxt_wr
  56 cases are for nxt_rd!=nxt_wr, so empty==0 and full==0
  8 cases are for nxt_rd==nxt_wr
  one set of 8 is for data_counter==0, so empty==1 (and full==0)
  one set of 8 is for data_counter==8, so full==1 (and empty==0)
  empty and full are not both asserted at the same time
Revised format of coverage model:
  (nxt_rd, nxt_wr, empty, full)
  total size of coverage space: 8*8*2*2 = 256 coverage tasks
  Encode assumptions into properties
  Only 56+8+8 = 72 coverage tasks are legal and meaningful.
It is worth noting the close link of the above coverage model to the properties for formal verification.
Defining meaningful functional coverage requires design understanding and engineering skill.

## Slide 21: Constraint Pseudo Random Test Generation

## Slide 22: Advanced TB Architecture
Constrained pseudo-random stimulus generation
Self-checking TB
  Monitors, Scoreboarding
Coverage Collection and Analysis
Promote a Coverage-Driven Verification Methodology
Scoreboard & Checkers
Stimulus Generator
Coverage Collector
Driver
Monitor
DUV
Monitor
Slave
Captures complete interface protocols by combining several checkers.
A smart data structure that captures what happens in the DUV during simulation. Often combined with checkers.
Constrained such that tests meet scenarios in the verification plan.

## Slide 23: Test Scenarios Matrix – Advanced
Description | Test # | Topic
Data is not modified | 2.1 | Data checking
 | 2.2 | 
 | 2.3 | 
 | 2.4 | 

## Slide 24: Test Scenarios Matrix – Advanced
Description | Test # | Topic
Data is not modified | 2.1 | Data checking
Data is not lost | 2.2 | 
Data is not duplicated | 2.3 | 
Data order is maintained | 2.4 | 
Basic scoreboard functionality.

## Slide 25: Test Scenarios Matrix – Advanced
Description | Test # | Topic
Data is not modified | 2.1 | Data checking
Data is not lost | 2.2 | 
Data is not duplicated | 2.3 | 
Data order is maintained | 2.4 | 
Reading and writing at the same time | 2.3 | Corner cases
 | 2.3.1 | 
 | 2.3.2 | 
 | … | 
 | … | 
 | … | 

## Slide 26: Test Scenarios Matrix – Advanced
Description | Test # | Topic
Data is not modified | 2.1 | Data checking
Data is not lost | 2.2 | 
Data is not duplicated | 2.3 | 
Data order is maintained | 2.4 | 
Reading and writing at the same time | 2.3 | Corner cases
 | 2.3.1 | 
 | 2.3.2 | 
 | … | 
 | … | 
 | … | 

## Slide 27: Test Scenarios Matrix – Advanced
Description | Test # | Topic
Data is not modified | 2.1 | Data checking
Data is not lost | 2.2 | 
Data is not duplicated | 2.3 | 
Data order is maintained | 2.4 | 
Reading and writing at the same time | 2.3 | Corner cases
Reading and writing at the same time when empty | 2.3.1 | 
Reading and writing at the same time when full | 2.3.2 | 
... at the same time as clearing | … | 
 | … | 
 | … | 
Should we rely on random generation by constraining stimulus to make these rare events happen more often?
How?
These make interesting functional coverage scenarios.

## Slide 28: Bug Hunting

## Slide 29: Given the following bug...
Concurrent reading from and writing to FIFO
  Should the data counter change its value?

## Slide 30: Given the following bug...
Concurrent reading from and writing to FIFO
  ok, the data counter should not change its value
  unless reading from and writing to the same data slot
  this only happens when the FIFO is
    empty: When the FIFO is empty and there is a write at the same time as a read (from empty), then the read should be ignored.
    full: When the FIFO is full and there is a read at the same time as a write, then the write (to full) should be ignored.
  But the logic that controls the value of the data counter does not distinguish these special cases.
  What do we need to do to find these bugs?

## Slide 31: Read/Write when FIFO is empty

## Slide 32: Read and Write when FIFO is full
Long test sequence to expose the bug.

## Slide 33: ABV

## Slide 34: Properties of the DUV
Black box view:
  Empty and full are never asserted together.
  After clear the FIFO is empty.
  After writing 8 data items the FIFO is full.
  Data items are moving through the FIFO unchanged in terms of data content and in terms of data order.
  No data is duplicated.
  No data is lost.
  data_out_valid only for valid data, i.e. no x’s in data.
An invariant property.

## Slide 35: Properties of the DUV
White box view:
  The value range of the read and write pointers is between 0 and 7.
  The data_counter ranges from 0 to 8.
  The data in the FIFO is not changed during a clear.
  For each valid read the read pointer is incremented.
  For each valid write the write pointer is incremented.
  Data is written only to the slot indicated by nxt_wr.
  Data is read only from the slot indicated by nxt_rd.
  When reading and writing the data_counter remains unchanged.
    What about a RW from an empty/full FIFO?

## Slide 36: Property Formalization

## Slide 37: Formalization of key DUV Assertions
  System Verilog Assertions (SVA) for:
    Empty and full are never asserted together.
      property not_empty_and_full;
      @(posedge clk) !(empty && full);
      endproperty
      assert property (not_empty_and_full);
    After clear the FIFO is empty.
      property empty_after_clear;
      @(posedge clk) (clear |=> empty==1);
      endproperty
      assert property (empty_after_clear);
    On empty after one write the FIFO is no longer empty.
      property not_empty_after_write_on_empty;
      @ (posedge clk) (empty && wr |=> !empty);
      endproperty
      assert property (not_empty_after_write_on_empty);
    Assertions can be monitored during simulation.
    Assertions can also be used for formal property checking.
    Challenge:
    There are many more interesting assertions.

## Slide 38: Corner case properties
FIFO empty: When the FIFO is empty and there is a write at the same time as a read (from empty), then the read should be ignored.
    property empty_write_ignore_read;
    @(posedge clk){empty && wr && rd |=>
    data_counter == $past(data_counter)+1};
    endproperty
    assert property (empty_write_ignore_read);
    cover property (empty_write_ignore_read);
FIFO full: When the FIFO is full and there is a read at the same time as a write, then the write (to full) should be ignored.
      property full_read_ignore_write
      @ (posedge clk) {full && rd && wr |=>
      data_counter == $past(data_counter)-1};
      endproperty
      assert property (full_read_ignore_write);
      cover property (full_read_ignore_write);

## Slide 39: Formal Property Checking

## Slide 40: Functional Verification Approaches
Verification
Reviews
Dynamic
Static
Prototyping
Simulation
Formal
Code
Analysis
Dynamic Formal
Linters
Theorem
Proving
Property
Checking
Equivalence
Checking
Silicon
FPGA
Emulation
Hybrid
Notes: Point out that Equivalence Checking is the most common form of Formal Verification now routinely used in practice.
Point out that it should not be confused with Property Checking.
Point out that Property Checking is also called Model Checking.

## Slide 41: Formal Property Checking
Properties of a design are formally proven or disproved.
Used to check for generic problems or violations of user-defined properties of the behaviour of the design.
Usually employed at higher levels of abstractions.
Give a
reconvergence model
for
formal property checking!
A reconvergence model is a conceptual representation of the verification process.
It helps us understand what is being verified.
Notes: A reconvergence model is a conceptual representation of the verificaiton process. It helps us understand what is being verified.

## Slide 42: Formal Property Checking
under env_constraint if condition then expectation
Properties of a design are formally proven or disproved.
Used to check for generic problems or violations of user-defined properties of the behaviour of the design.
Usually employed at higher levels of abstractions.
Properties are derived from the specification. (interpretation step)
Properties are expressed as formulae in some (temporal) logic.
RTL
Specification
Interpretation
Properties (Assertions)
RTL Coding
Interpretation
Property Formalization

## Slide 43: Formal Property Checking
Properties of a design are formally proven or disproved.
Used to check for generic problems or violations of user-defined properties of the behaviour of the design.
Usually employed at higher levels of abstractions.
Properties are derived from the specification. (interpretation step)
Properties are expressed as formulae in some (temporal) logic.
Checking is typically performed on a Finite State Machine model of the design.
  This may be the RTL.
RTL
Specification
Interpretation
Properties (Assertions)
RTL Coding
Interpretation
Property Formalization
Property Checking
Property checking can also be preformed on higher levels of abstraction.

## Slide 44: Simulation vs Functional Formal Verification
In practice, completeness issues and capacity limits restrict formal verification to selected parts of the design.
Naïve interpretation of exhaustive formal verification:
Only selected parts of the design can be covered during simulation.
[B. Wile , J.C. Goss and W. Roesner, “Comprehensive Functional Verification – The Complete Industry Cycle”, Morgan Kaufman, 2005]
Verify ALL properties.
Challenge 1:
Specify properties to cover the entire design.
Challenge 2:
Prove all these properties.
Notes: Distinction between reachable and possible states will be demonstrated using Jasper on the FIFO design.
Discuss the meaning of ALL properties: How do we know we have ALL properties?

## Slide 45: The Role of Formal Property Checking
Property Checking is the most common form of high-level formal verification used in practice.
  Property checking is fully automatic.
    Requires the properties to be written.
  It performs exhaustive verification of the design wrt the specified properties.
  It provides proofs and can demonstrate the absence of bugs.
  A counter example is presented for failed properties.
  Used for critical well specified parts of the design
    Cache coherence protocols, Bus protocols, Interrupt controllers
Formal Methods can suffer from capacity limits
  There are tried and trusted techniques to overcome these:
    Start with narrow focus on block level, work up towards higher levels in the design hierarchy turning asserts into assumes
    Restrict property checking to work over finite small time windows.
    Limit environment behaviour by strengthening constraints.
    Case splits over a set of properties, partitioning and black boxing.

## Slide 46: Outcomes of Formal Property Checking
Formulate Property
Invoke Property Checker
Property proven
Property fails
Property is trivially true
Vacuity check
Bug in
Property
Property is non-trivially true
DUV satisfies Property
Counter example (CE)
Unreach-able
Reach-able
DUV bug detected
Reach-able other CE exists
No reach-able other CE exists
Bug in Property
DUV bug detected

## Slide 47: Outcomes of Formal Property Checking
Formulate Property
Invoke Property Checker
Property proven
Property fails
Property is trivially true
Vacuity check
Bug in
Property
Property is non-trivially true
DUV satisfies Property
Counter example (CE)
Unreach-able
Reach-able
DUV bug detected
Reach-able other CE exists
No reach-able other CE exists
Bug in Property
DUV bug detected
Most common mistake, restrict input space so much that property becomes trivially true.
Specify environment constraints for proof.
Under-constrained properties may lead to unreachable counter examples.
Correctness of proof relies on correctness of the environment constraints.

## Slide 48: How do you know you’ve encoded the property right?
Keep properties and sequences simple.
  Build complex properties from simple, short properties
But if the property succeeds, how do you know whether you’ve encoded the property right?
Peer review properties you write.
If the property fails,
you can investigate the counter example:
  Is it reachable or not?

## Slide 49: Formal Property Checking
Property checking tools can formally verify assertions.
  Basic properties (visualize):
    Basic functionality
    Range checks
  Re-use SV Assertions as properties (check):
    Empty and full are never asserted together.
    After clear the FIFO is empty.
    On empty after one write the FIFO is no longer empty.
  Understanding counter examples:
    Debug an assumption
    Debug a design property
Closely related to functional coverage.
Link from env_constraints to simulation assertions.
Note:

## Slide 50: Formal Property Checking
Jasper DEMO
  Formal verification of selected FIFO properties from ABV

## Slide 51: How big is Exhaustive?
Consider simulating a typical CPU design
  500k gates, 20k DFFs, 500 inputs
  70 billion sim cycles,
  running on 200 linux boxes for a week
  How big: 236 cycles
Consider formally verifying this design
  Input sequences: cycles 2(inputs+state) = 220500
  What about X’s: 215000 (5,000 X-assignments + 10,000 non-reset DFFs)
  How big: 220500 cycles (215000 combinations of X is not significant here!)
That’s a big number!
  Cycles to simulate the 500k design: 236 (70 billion)
  Cycles to formally verify a 32-bit adder: 264 (18 billion billion)
  Number of stars in universe: 270 (1021)
  Number of atoms in the universe: 2260 (1078)
  Possible X combinations in 500k design: 215000 (104515 x 3)
  Cycles to formally verify the 500k design: 220500 (106171)
Simulasaurus

## Slide 52: Summary
Block-level Case Study
  Specification
  Verification Plan
  Directed Testing
  (Code Coverage)
  Functional Coverage
  Assertion-based Verification
  Formal Property Checking
No single method is adequate to cover a whole design in practice.
  Carefully select the verification methods that maximize ROI.
  Complement simulation with formal: Integrated approach