## Slide 1: High-level Verification with specman and e
Kerstin Eder
Design Automation and Verification
Department of
COMPUTER SCIENCE

## Slide 2
“Improving Shareholder Value by Separating Verification from Design”
The semiconductor industry continues to strive to manage the ever increasing risk of leaving a corner case bug that becomes the next front page story for EETimes. With cost of failure fast becoming a common agenda point in many semiconductor board room meetings around the world, how can you deliver to the ever growing demands of increasing shareholder value?
Managing scarce resources to deliver sustainable competitive advantage is the platform upon which most of today's strategic thinking is built. Yet in the complex world of semiconductor product design we continue to see the promotion of the “jack of all trades’” designer in the false belief that it actually reduces costs.
Separating verification from design is a natural evolution to the necessary specialization that has become functional verification today. Why do accounting regulations demand that you employ armies of auditors to review your end of year accounts? When, not so many years ago, you could get away with your own accountants completing this function.
Auditors are much the same as verification engineers. They are approaching the problem from a completely different perspective. They do not come with the cognitive incompetence of “I know that's right, because I produced it!” The global company graveyard is littered with the tomb-stones of many household names that have made this mistake, Enron included.
In this presentation, Verisity will deliver a solution to provide unique value that can be generated when you separate the concerns of functional verification from design. Reducing the cost of failure risks and significantly improving the effectiveness of your scarce engineering resource by automating the process of verification itself.
  Presenter at edaForum04, Dresden, Germany, December 9th/10th 2004:
  Coby Hanoch, Senior Vice President of Sales, Verisity Design, Inc.

## Slide 3: High-level Verification
State-of-the-art Verification Methodology
  Focus on Automation of the Verification Process
  Tools: now from Cadence (who bought Verisity in April 2005)
    Specman Elite (SN) and
    “e” verification language
Aim:
  Raise level of abstraction, enable automation and, thus, enhance productivity.
For local configuration info see:
  Exercise 4: Intro to Specman Tutorial.
  [Please work your way through the on-line Specman intro tutorial.]
[Credits: The material for this lecture is adapted from Verisity training material.]

## Slide 4: SN Main Enabling Technologies
Constraint-driven Test Generation
  Create lots of meaningful tests quickly. 
  Control over automatic test generation.
  Capture constraints from spec and verification plan.
Data and Temporal Checking
  Self-checking modules ensure data correctness and temporal properties.
  Checks are always active.
    Unless turned off by: set check IGNORE ;-)
Functional Coverage Collection and Analysis
  Automatic functional coverage collection.
  Analyse progress against functional coverage metrics.
Promotes Coverage Driven Verification (CDV)

## Slide 5: SN Verification Automation

## Slide 6: Complete SN Verification Process
Verification Plan
Coverage Metrics
Test Cases
DUV Spec
Test 1
Test 2
Test n-1
Test n
Driving Stimulus
Collecting Output
Coverage
Generating Stimulus
Checking
DUV
Testbase
The key is the Verification Plan!

## Slide 7: Complete SN Verification Process
Verification Plan
Coverage Metrics
Test Cases
DUV Spec
Test 1
Test 2
Test n-1
Test n
Driving Stimulus
Collecting Output
Coverage
Generating Stimulus
Checking
DUV
Testbase
The key is the Verification Plan!
Coverage-driven stimulus generation

## Slide 8
Hollander, Y.; Morley, M.; Noy, A., "The e language: a fresh separation of concerns," in Technology of Object-Oriented Languages and Systems, 2001. TOOLS 38. Proceedings , vol., no., pp.41-50, 2001 DOI: 10.1109/TOOLS.2001.911754

## Slide 9: Basics of the “e” Language
High-level language for writing verification environments:
  test benches
  coverage collection
  test generation and checking
“e” supports:
  Modular aspect-oriented design
  high-level data types
  pseudo-random constrained-based data generation
  events
  high-level checking
  checking of basic timing properties
An “e” component is a representation of the “rest of the world” as seen from an interface of the DUV.

## Slide 10: Aspect-oriented Programming
AOP is the “next step up” from object-oriented programming.
  Testcases have specific purposes:
    Does parity check on packets work?
    Are timing properties of transmission protocol valid?
  Both are different concerns: They are orthogonal!
  Two aspects of same application DUV.
AOP provides mechanisms to separate these two concerns into separate aspects of the verification environment.
Well-defined techniques for adding declarations, inserting or replacing code from the outside of a class, without editing the original class.

## Slide 11: On-line Help
All Specman and “e” language help is on-line:
  e language reference
  Command reference for Specman Elite
  User guide etc.
For sn and “e” help use sn_help.sh from command line.
  Make sure you change to “Tree View”!
  Go to “Edit” menu.
  Select “Settings”.
  Tick “Show Tree View on startup’”.
For IUS/ncsim help use cdnshelp from command line.

## Slide 12: File Format
An “e” code segment is enclosed with a begin-code marker <‘ and an end-code marker ‘>.
  Both the begin-code marker and the end-code markers must be placed at the beginning of a line (left-most), with no other text on that same line.
Example “e” code segment:
    <‘
    import cpu_test_env;
    ‘>
Several code segments can appear in one file, each segment consists of one or more statements.

## Slide 13: Comments
“e” files begin with a comment!
This comment ends when first begin-code marker <‘ is found.
Comments in code segments can be marked with – or //.
Use end-code ‘> and begin-code <‘ markers to write several consecutive lines of comment in the middle of code segments.
Notes: WHY is this a good idea? Discuss

## Slide 14: Syntactic Elements
Statements are top-level constructs.
  Valid within <‘ and ‘> markers.
  Statements always end with a semicolon “;”!
Struct members are second-level constructs.
  Valid only within a struct definition.
  They are associated with dynamic constructs of a testbench e.g. stimulus.
  (There are also Units which are associated with testbench constructs such as drivers/checkers/scoreboards. They exist for the duration of the simulation.)
Actions are third-level constructs.
  Valid only when associated with a struct member, such as a method or an event.
Expressions are lower-level constructs.
  Can be used only within another “e” construct.

## Slide 15: Key Statements Types
struct Defines a new data structure.
unit Defines a new unit.
type Defines an enumerated type or subtype.
extend Extends a previously defined struct/type.
define Extends language.
  define OFFSET 5;
import must be first (after defines),
otherwise the order of statements is not
critical.
... (more, see on line doc)

## Slide 16: Structs vs Units
Structs are the most basic building blocks in “e”.
  Used to keep data and operations together.
    packets, instructions, frames
  Can be created at run-time, i.e. they are dynamic.
  Data can be generated on-the-fly.
Units are a special kind of struct.
  Units are static! Can be generated during test phase only.
  Allow mapping to HDL path. (Best way to connect to DUV.)
Used for generators/checkers/monitors, bus functional models (BFMs), self-checking structures, overall testbench.
  BFMs package all bus functional procedures of an interface, i.e. all transactions supported by the interface.
  The transactions are abstracted from a physical-level interface to a procedural interface.
  BFMs can be used to generate stimulus as well as to check the DUV response.

## Slide 17: Structs and Struct Members
Members are 2nd-level constructs: Valid only within a struct definition.
  A simple struct for packets to be used in comms protocol:
    type packet_kind: [atm, eth];
    struct packet {
    len: int;
    keep len < 256;
    kind: packet_kind;
    };
  keep: Specifies rules for constraints to influence data generation.
  Another example struct for transactions:
    struct transaction {
    address: uint;
    data: list of uint;
    transform(multiple:uint) is empty;
    };

## Slide 18: Struct Members
Field: Defines data entry to be a member of the enclosing struct with explicit data type.
Method: Defines operational procedure that can manipulate fields of enclosing struct and access run-time values in DUV.
Subtype declaration: Defines instance of parent struct in which specific members have particular values or behaviour.
  Use when for conditional constraints on possible values of a field.
Constraint declaration: Influences distribution of values generated for data entries and the order in which values are generated, e.g. keep len < 256;
Coverage declaration: Defines functional verification goals and collects data on how well the testbench is meeting these goals.
  cover event-type is coverage-item-definition;
Temporal declaration: Defines “e” events and their associated actions, e.g. event

## Slide 19
type PCICommandType: [ IO_READ=0x2, IO_WRITE=0x3,
MEM_READ=0x6, MEM_WRITE=0x7 ];
struct pci_transaction like transaction {
command : PCICommandType;
keep soft data.size() in [0..7];
dual_address: bool;
when dual_address pci_transaction {
address2: uint;
};
bus_id: uint;
event initiate;
on initiate {
out("An event was initiated on bus ”, bus_id);
};
cover initiate is {
item command;
};
transform(multiple:uint) is only {
address = address * multiple;
};
};

## Slide 20
type PCICommandType: [ IO_READ=0x2, IO_WRITE=0x3,
MEM_READ=0x6, MEM_WRITE=0x7 ];
struct pci_transaction like transaction {
command : PCICommandType;
keep soft data.size() in [0..7];
dual_address: bool;
when dual_address pci_transaction {
address2: uint;
};
bus_id: uint;
event initiate;
on initiate {
out("An event was initiated on bus ”, bus_id);
};
cover initiate is {
item command;
};
transform(multiple:uint) is only {
address = address * multiple;
};
};
struct
field
field
field

## Slide 21
type PCICommandType: [ IO_READ=0x2, IO_WRITE=0x3,
MEM_READ=0x6, MEM_WRITE=0x7 ];
struct pci_transaction like transaction {
command : PCICommandType;
keep soft data.size() in [0..7];
dual_address: bool;
when dual_address pci_transaction {
address2: uint;
};
bus_id: uint;
event initiate;
on initiate {
out("An event was initiated on bus ”, bus_id);
};
cover initiate is {
item command;
};
transform(multiple:uint) is only {
address = address * multiple;
};
};
constraint declaration

## Slide 22
type PCICommandType: [ IO_READ=0x2, IO_WRITE=0x3,
MEM_READ=0x6, MEM_WRITE=0x7 ];
struct pci_transaction like transaction {
command : PCICommandType;
keep soft data.size() in [0..7];
dual_address: bool;
when dual_address pci_transaction {
address2: uint;
};
bus_id: uint;
event initiate;
on initiate {
out("An event was initiated on bus ”, bus_id);
};
cover initiate is {
item command;
};
transform(multiple:uint) is only {
address = address * multiple;
};
};
type definition
subtype definition

## Slide 23
type PCICommandType: [ IO_READ=0x2, IO_WRITE=0x3,
MEM_READ=0x6, MEM_WRITE=0x7 ];
struct pci_transaction like transaction {
command : PCICommandType;
keep soft data.size() in [0..7];
dual_address: bool;
when dual_address pci_transaction {
address2: uint;
};
bus_id: uint;
event initiate;
on initiate {
out("An event was initiated on bus ”, bus_id);
};
cover initiate is {
item command;
};
transform(multiple:uint) is only {
address = address * multiple;
};
};
method

## Slide 24
type PCICommandType: [ IO_READ=0x2, IO_WRITE=0x3,
MEM_READ=0x6, MEM_WRITE=0x7 ];
struct pci_transaction like transaction {
command : PCICommandType;
keep soft data.size() in [0..7];
dual_address: bool;
when dual_address pci_transaction {
address2: uint;
};
bus_id: uint;
event initiate;
on initiate {
out("An event was initiated on bus ”, bus_id);
};
cover initiate is {
item command;
};
transform(multiple:uint) is only {
address = address * multiple;
};
};
event
coverage declaration

## Slide 25: Predefined Structs
An “e” environment contains by default a number of predefined structs (and of course some user-defined ones).
The system struct sys is the root for user-defined structs.
  Must instantiate user-defined structs under sys.
  Contents of sys can be viewed via SN GUI.
Similar to main in C.
global
packing
session
files
sys
scheduler
simulator
all user-defined

## Slide 26: Instantiation under sys
Every user-defined struct (including units) must be instantiated as a (sub)field of sys, e.g.
    struct packet {
    address : uint (bits : 2);
    payload : uint (bytes : 64);
    };
    unit router_bfm {
    packets : list of packet;
    };
    extend sys {
    router : router_bfm is instance;
    };

## Slide 27: Generation with SN
Offline (prior to sim, i.e. in Generate phase):
  Use Generate or Test command
    Test calls Generate command!
  Recursively generates everything under sys.
  BEWARE: Can consume a lot of memory!
Online (during sim):
  Use gen action.
    gen gen-item [keeping {...}]
  Allows to dynamically generate values based on DUV state.

## Slide 28: Using Constraints
keep constraint-bool-expr;
  where constraint-bool-expr is a simple or compound Boolean expression.
States restriction on the values generated for fields in the struct.
  keep kind!=tx or len==16;
Describes required relationships between field values and other struct items.
  struct packet {
  kind : [tx, rx];
  len : int;
  keep kind == tx => len==16;
  --when tx packet { keep len == 16; }; exactly same effect
  };
Hard constraints are applied when the enclosing struct is generated. If constraints can't be met, generator issues constraint contradiction message.

## Slide 29: Generation with keep
Generation order is important:
  It influences the distribution of values!
    struct packet {
    kind : [tx, rx];
    len : int;
    keep len > 15 => kind==rx;
    };
  If kind is generated first, kind is tx about half the time because there are only two legal values for kind.
  If len is generated first, the distribution is different.
  Consider using: keep gen (kind) before (length);

## Slide 30: Using Soft Constraints
Using keep soft (e.g. to set default values) and select:
    struct transaction {
    address : uint;
    keep soft address == select {
    10: [0..49];
    60: 50;
    30: [51..99];
    };
    };
NOTE: Soft constraints can be overridden by hard constraints!
    extend instruction {
    keep soft op_code == select {
    40: [ADD, ADDI, SUB, SUBI];
    20: [XOR, XORI];
    10: [JMP, CALL, RET, NOP];
    };
    };
In practice, getting the weights/bias right (for coverage closure) requires significant engineering skill.

## Slide 31: Randomized Test Generation needs…
... repeatability:
  Same testbench version + same test
  + same random seed
  = same stimulus data.
Is this all? The testbench evolves over time!

## Slide 32: Randomized Test Generation needs…
Repeatability:
  Same testbench version + same test
  + same random seed
  = same stimulus data.
Random stability:
Changes to the testbench should not affect orthogonal aspects!
  Packet data structure:
    struct packet {
    ...
    payload: list of byte;
    ...};

## Slide 33: Randomized Test Generation needs…
Repeatability:
  Same testbench version + same test
  + same random seed
  = same stimulus data.
Random stability:
Changes to the testbench should not affect orthogonal aspects!
  Packet data structure with new interrupted field:
    struct packet {
    ...
    payload: list of byte;
    interrupted: bool;
    ...};
  With same seed we should get the same payload data!

## Slide 34: Packing: Driving Stimulus into the DUV
pack() function:
pack() is a Specman Elite system function.
  pack(option:pack option, item: exp, ...): list of bit
Converts higher-level data structure to bit stream required by DUV.
  i_stream = pack(packing.high, opcode, op1, op2);
pack options are: packing.high, packing.low or NULL
  packing.high: 1st item at MSB
  packing.low: 1st item at LSB
  NULL: Use global default - set initially to packing.low.
item: A legal “e” expression that is a path to a scalar or a compound data item, such as a struct, field, list, or variable.

## Slide 35: Packing High
packing.high: 1st item at MSB
input_stream = pack(packing.high,addr, data);
packet.addr = 2’b11; 11
packet.data[0] = 0xaa; 10101010
packet.data[1] = 0xee; 11101110
17……………………………………………0
input_stream = 11 10101010 11101110

## Slide 36: Packing Low
packing.low: 1st item at LSB
input_stream = pack(packing.low,addr, data);
packet.addr = 2’b11; 11
packet.data[0] = 0xaa; 10101010
packet.data[1] = 0xee; 11101110
17……………………………………………0
input_stream = 11101110 10101010 11

## Slide 37: Fields
[!][\%] field-name[:type] [[min-val..max-val]] [((bits | bytes):num)]
    ! Denotes an ungenerated field.
    % Denotes a physical field.
  The type for the field can be any scalar type, string, struct, or list.
  (bits | bytes: num) specifies width of field in bits or bytes.
    type NetworkType: [IP=0x0800, ARP=0x8060] (bits: 16);
    struct header {
    %address: uint (bits: 48);
    %length: uint [0 .. 32];
    };
    struct packet {
    hdr_type: NetworkType;
    %hdr: header;
    is_legal: bool;
    !counter: uint;
    };
Field order is important!
  It is the packing order for physical fields.

## Slide 38: Physical Fields
Marked with %.
Physical fields are packed when the struct is packed.
Used for fields that represent data that will be sent to HDL design in the simulator.
If no range is specified, width of field is determined by field's type.
If the field's type does not have a known width, you must use (bits | bytes: num) syntax to define the width.
  (Important for packing!)
Non-physical fields are called virtual fields.
They are not packed automatically when the struct is packed.
  (They can be packed individually if needed.)

## Slide 39: Ungenerated Fields
Marked with !
  Values for these fields are not auto generated.
  Useful for fields that:
    Are explicitly assigned values during verification.
    Must contain values whose computation is too complicated to be expressed with constraints.
  Ungenerated fields get default initial value:
    0 for scalars, NULL for structs and empty list for lists.
    Ungenerated fields whose value is from a range (e.g. [20..30]) get initialized to the first value in range.
    If the field is a struct it won't be allocated and none of the fields in it will be generated.

## Slide 40: Limitations of e's AOP Implementation
(Too) Many things can be extended!
  So more discipline and structure is required.
Fields can only be appended:
  Fields are physically appended to existing fields
  Might create a problem when packing!
Variance control fields: Extensions can only be specified for a single value of the control field.
  Instructions SHL and SHR have a feature that applies to both.
  Needs to be specified for both, or use the following trick!

## Slide 41
Extensions via variance control fields can only be specified for a single value of the control field!
  To get around this, introduce an additional virtual field.
  This field controls the common extensions.
  Example: Extension to an instruction struct (for Calc_1 design):
  type opcode_t : [ NOP, ADD, SUB, INV, INV1, SHL, SHR ] (bits : 4);
  struct instruction_s {
  %cmd_in : opcode_t;
  %din1 : uint (bits:32);
  %din2 : uint (bits:32);
  !resp : uint (bits:2);
  !dout : uint (bits:32);
  check_response(ins : instruction_s) is empty;
  }; // struct instruction_s
  extend instruction_s {
  is_a_shift : bool;
  keep is_a_shift == opcode in [SHL, SHR];
  when is_a_shift instruction_s {
  // Common extension to SHL and SHR goes below.
  ...
  }
  }

## Slide 42: Limitations of e's AOP Implementation
(Too) Many things can be extended!
  So more discipline and structure is required.
Fields can only be appended:
  Fields are physically appended to existing fields
  Might create a problem when packing!
Variance control fields: Extensions can only be specified for a single value of the control field.
  Instructions SHL and SHR have a feature that applies to both.
  Needs to be specified for both, or use the following trick!
Methods can only be appended, prepended or replaced.
Aspects are order-dependent (on loading).

## Slide 43: Synch between SN and Simulator
Specman
Simulator
SN executes presim phase
SN gives control to simulator
Sim runs until value of a signal attached to an @sim event changes. Issues callback and sim suspends.
Sim continues until next callback.
Callback triggers all SN events attached to @sim event.
SN evaluates TEs, emits events and executes TCMs.
callback
sys.tick_start
sys.tick_end
t=0 ns
t=N ns
t=N ns
Issue Test command
time

## Slide 44: SN Predefined Event: @sim
event clk is rise (clk_p$) @sim;
@sim is a special sampling event.
@sim occurs at any simulator callback.

## Slide 45: Synch between SN and Simulator
Specman
Simulator
SN executes presim phase
SN gives control to simulator
Sim runs until value of a signal attached to an @sim event changes. Issues callback and sim suspends.
Sim continues until next callback.
Callback triggers all SN events attached to @sim event.
SN evaluates TEs, emits events and executes TCMs.
callback
sys.tick_start
sys.tick_end
t=0 ns
t=N ns
t=N ns
Issue Test command
time

## Slide 46: SN Predefined Event: @sim
event clk is rise (clk_p$) @sim;
@sim is a special sampling event.
@sim occurs at any simulator callback.
  Expression must be an HDL signal path in the simulated model.
Signal does not have to be a clock.
  No restriction for signal to be periodic or synchronous.
Heavy use of @sim events might slow down simulation!
  Clock signal can also be emitted from “e” code and driven into DUV. (But usually more efficient to generate clock in HDL.)
When not running with a simulator attached to SN, use @sys.any.

## Slide 47: Events in SN
Events are struct members.
Events are used to synchronize with the DUV or to debug a test.
Automatic emission of events:
  <'
  extend driver_s {
  event clk is fall(clk_p$) @sim;
  event resp is change(out_resp1_p$)@clk;
  };
  ’>

## Slide 48: Events in SN
Events are struct members.
Events are used to synchronize with the DUV or to debug a test.
Explicit emission of event:
  <'
  extend driver_s {
  collect_response(cmd : command_s) @clk is also {
  emit cmd.cmd_complete;
  };
  };
  ’>

## Slide 49: Advanced Techniques: SN temporal checking
SN Temporal Language
Capture behaviour over time for synchronization with DUV, functional coverage and protocol checking.
Language consists of:
  temporal expressions (TEs)
  temporal operators
event struct members to define occurrences of events during sim run
expect struct members for checking temporal behaviour
PSL/Sugar and SVA compatible expressions.

## Slide 50: Temporal Expressions in “e”
Each TE is associated with a sampling event.
Sampling event indicates when the TE should be evaluated by SN.
Syntax examples:
  true(boolean-exp)@sample-event
  rise/fall/change(expression)@sample-event

## Slide 51: Temporal Checking Methodology
Capture important DUV temporal behaviour with events and TEs.
Use expect struct members to declare temporal checks.
expect TE else dut_error(string);
Example temporal checks:
    expect @req => {[..4];@ack} @clk
    else dut_error("Acknowledge did not follow
    request within 1 to 5 clock cycles.");
    expect @buffer_full => eventually @int @clk
    else dut_error("Buffer full, but interrupt did not
    occur.");
  eventually means sometime before the end of simulation!

## Slide 52: Conforming to Stimulus Protocol
Need be able to react to state of DUV during simulation!
  clock, signal changes, sequences of events
“e” language provides wait (till next cycle) and sync actions which allow to pause procedural code until event occurs.
    print a;
    wait true(enable_p$==1)@clk;
    print b;
    print a;
    sync true(enable_p$==1)@clk;
    print b;
t0
t1
t2
print a;
enable
clk
print b;
print a;
print b;

## Slide 53: Methods with a Notion of Time
TCMs - Time Consuming Methods
  Depend on sampling event.
  Can be executed over several simulation cycles.
collect_response(cmd : command_s) @clk is {
wait @resp; -- wait for the response
cmd.resp = out_resp1_p$;
cmd.dout = out_data1_p$;
}; // collect_response
  Implicit synchronization action at beginning of TCM.

## Slide 54: Methods with a Notion of Time
TCMs - Time Consuming Methods
  TCM must be called or started to execute.
    run() is also {
    start drive(); // spawn
    }; // run
  Non-TCMs can't call TCMs because they have no notion of time.
  TCMs can (only) be started (using start) from a non-TCM!

## Slide 55: Synch between SN and Simulator
Specman
Simulator
SN executes presim phase
SN gives control to simulator
Sim runs until value of a signal attached to an @sim event changes. Issues callback and sim suspends.
Sim continues until next callback.
Callback triggers all SN events attached to @sim event.
SN evaluates TEs, emits events and executes TCMs.
callback
sys.tick_start
sys.tick_end
t=0 ns
t=N ns
t=N ns
Issue Test command
time

## Slide 56
Advanced Checking:
Scoreboarding in e
(this refers back to the lecture on checking)
DUV
Scoreboard
OK?

## Slide 57: Scoreboarding in e - 1
Assume: DUV does not change order of packets.
  Hence, first packet on scoreboard has to match received packet.
  import packet_s;
  unit scoreboard {
  !expected_packets : list of packet_s;
  add_packet(p_in : packet_s) is {
  expected_packets.add(p_in);
  };
  check_packet(p_out : packet_s) is {
  var diff : list of string;
  -- Compare physical fields of first packet on scb with p_out.
  -- Report up to 10 differences.
  diff = deep_compare_physical(expected_packets[0], p_out, 10);
  check that (diff.is_empty())
  else dut_error(‘‘Packet not found on scoreboard.’’,diff);
  -- If match was successful, continue.
  out(‘‘Found received packet on scoreboard.’’);
  expected_packets.delete(0);
  };
  };

## Slide 58: Scoreboarding in e - 2
Recording a packet on the scoreboard:
  Extend driver such that
  When packet is driven into DUV call add_packet method of scoreboard.
    Current packet is copied to scoreboard.
  It is useful to define an event that indicates when packet is being driven.
Checking for a packet on the scoreboard:
  Extend receiver such that
  When a packet was received from DUV call check_packet.
    Try to find the matching packet on scoreboard.
  It is useful to define an event that indicates when a packet is being received.

## Slide 59: Specman Elite Tutorial
DUV: simple CPU (ALU, 4 regs, PC, PC_Stack, fetch/exec FSM)
  Interface: clock, reset, instruction [8 bit]
Learn how to:
  Design the verification environment
  Define DUV interfaces
  Generate a simple test
  Drive and check the DUV
  Generate constraint-driven tests
  Define and analyse test coverage
  Create corner case tests
  Create temporal and data checks
  Analyse and bypass bugs
About 100 pages. A really easy “learn by doing” lab. Takes about 2h. 

## Slide 60: We have now covered
Basics of the “e” verification language.
  Please work though the Specman Elite Tutorial.
Next:
  Assignment 2 - Intro to .e code and verification method.
  Hands-on session with demo.